## Slide 1: Welcome to the Life Cycle Assessment (LCA) Learning Module Series
Acknowledgements:
CESTiCC Washington State University Fulbright
Liv Haselbach Quinn Langfitt
For current modules email haselbach@wsu.edu or visit cem.uaf.edu/CESTiCC

## Slide 2: LCA Module Series Groups
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules

## Slide 3: Introduction to Life Cycle Assessment and International Standard ISO 14040
Module A1

## Slide 4: What is Life Cycle Assessment?
    “Compilation and evaluation of the inputs, outputs and the potential environmental impacts of a product system throughout its life cycle”*
LIFE CYCLE ASSESSMENT (LCA)
    Process split into life cycle stages and LCA phases
      Stages are portions of the product life cycle and phases are the portions of the LCA process
    Data collected on inputs and outputs of the system
    Associated environmental and resource impacts of those inputs and outputs
*ISO 14040:2006

## Slide 5: Phases versus Stages
Inventory Analysis
Impact Assessment
Goal and Scope
Interpretation
Phases
  Portions of LCA procedure
Figure: ISO 14040:2006
Stages
  Sections of product life cycle
Manufacture
Disposal/recycling
Extraction and upstream production
Transport
Use
Transport
Transport
  Note: This is a general diagram of stages and some products or processes may have more or less stages than those shown here

## Slide 6: Principles of LCA
Guidance for product, process, or constructed element selection
Entire life cycle environmental burden between stages and processes
Relative to a functional unit
  Functional unit is a quantified amount of function obtained from the product or process
    Light bulb functional unit might be 1,000,000 lumen-hours of light
    Bus functional unit might be 10,000 passenger-kilometers traveled
  Covered more in α modules
Only environmental considerations addressed
  Economic, social, and other aspects could be considered with other tools
Iterative process where each phase uses results of other phases
  For example: goal and scope can and should be updated during analysis of other stages

## Slide 7: LCA Science
Comprehensiveness
  Attempt to cover all attributes or aspects of natural environment, human health and resources!
  Therefore, include a wide range of potential environmental impacts in LCA studies
  Coverage of every conceivable impact not possible
No scientific basis for generating a single overall score
  Must report individual impact scores
Priority of scientific approach to characterize impacts:
  First: Natural science
  Next: Social or economic science or International convention
  Last: Value choices (opinion, preferences)

## Slide 8: Why Do An LCA?
Identify opportunities to improve environmental performance
Inform decision-makers
Select relevant indicators of environmental performance
Marketing e.g. ecolabel

## Slide 9: ISO 14040 Background
LCA Principles and Framework
“Details the requirements for conducting an LCA”*
Also covers Life Cycle Inventory (LCI) only study
Developed first by the International Organization for Standardization (ISO) in 1996.
  Updated to second edition in 2006
Guiding document for basic Life Cycle Assessment procedures
  More detailed procedures and examples in:
    ISO 14044 – Requirements and guidelines
    ISO/TR 14047 – Illustrative examples on how to apply ISO 14044 to impact assessment situations
    ISO/TS 14071 – Critical review process and reviewer competencies: Additional requirements and guidelines to ISO 14044:2006
    ISO/TS 14048 – Data documentation format
*ISO 14040:2006
Course Module A2 dedicated to ISO 14044

## Slide 10: Scope of ISO 14040
ISO 14040 contains general information on:
  Goal and scope of LCA
  LCI phase
  LCIA phase
  Interpretation phase
  Reporting and critical review
  Limitations
  Relationship between phases
  Conditions for use of value choices and optional elements
Normative references: Need to use 14044 to apply 14040
Phases of an LCA

## Slide 11: Phases of an LCA
LCA
Phases
1. Goal and Scope
3. Life Cycle Impact Assessment (LCIA)
4. Interpretation
2. Life Cycle Inventory (LCI)
Image Sources: Target: wikia.nocookie.net Data: dreamstime.com Earth: business2community.com
Note: For an LCI study LCIA phase is omitted

## Slide 12: Phase 1: Goal and Scope
Scope follows the goal and provides background information, details methodological choices, and tells how the report will be formatted.
Goal
Goal statement is the first component of an LCA and guides much of the subsequent analysis
Goal must state:
Intended use
Reasons for study
Audience
Whether comparative and disclosed to public
Scope
Scope provides background information, details methodological choices, and lays out report format
Scope includes:
Product system
Functions of systems
Functional unit
System boundary
Allocation procedures
Impact categories, assessment method and interpretation type
  Data requirements
  Assumptions
  Limitations
  Initial data quality requirements
  Type of critical review, if any
  Type and format of report
More information on goal and scope are provided in Module A2 and the α modules

## Slide 13: Phases 2 and 3: LCI and LCIA
Life Cycle Inventory (LCI) Phase
  Data collection
  As much input and output data as possible is collected
  Can be presented in report or kept private, such as if confidentiality agreements warrant
  Useful for other researchers that could use that data
Life Cycle Impact Assessment (LCIA) Phase
  Conversion of inventory data into environmental impact potentials
  Impact categories, indication, and characterization models are chosen
  Data are grouped based on potential to cause certain environmental impacts (classification)
  Input and output quantities converted to potential impacts based on characterization factors (characterization)
  Optional steps: Normalization, grouping, weighting (more details in α modules)

## Slide 14: Phase 4: Interpretation
Continually ongoing during assessment to help guide other phases
Discussion of inventory analysis and impact assessment results in LCA study
  In an LCI study, only inventory needs to be discussed
Can be modeled as conclusions and recommendations to the decision maker
Should be consistent with and based on goal and scope of the study
Should reflect the various uncertainties inherent in LCA including:
  LCA is based on a relative approach using a functional unit
  Impacts are “potential”

## Slide 15: Limitations of LCA
*ISO 14040:2006
“Not a complete assessment of all environmental issues”* because only those identified in the goal and scope are considered
LCI can rarely, if ever, include every single process and capture every single input and output due to system boundaries, data gaps, cut-off criteria, etc.
LCI data collected contains uncertainty
Characterization models are far from perfect
Sensitivity and other uncertainty analyses are not fully developed

## Slide 16: Critical Review
Image: shenandoahchiropractic.com
Necessary component for comparative studies disclosed to the public
Verifies process and consistency with principles
  Not an endorsement
  Does not verify or validate goals
Can improve credibility of study
Critical review process defined in goal and scope!
External independent chair person and at least two other members

## Slide 17: Summary Features of an LCA
  Systematic procedure for environmental assessment through product or process life cycle
  Functional unit basis for comparisons differs from many other environmental management techniques
  Amenable to data confidentiality needs and proprietary matters
  Open to update based on new science and developing techniques
  Not overly restrictive
  Impacts identified are all expressed as POTENTIAL
  LCIA converts LCI results to environmental issues based on characterization factors
  Systematic approach to identify, check, evaluate and present information based on goal and scope
  Iterative process with continual interpretation
  May link to other environmental management techniques
Note: Features identified are based on those put forth in ISO 14040:2006

## Slide 18: Full Listing of Terms in ISO 14040
3.1 life cycle
3.2 life cycle assessment
3.3 life cycle inventory analysis
3.4 life cycle impact assessment
3.5 life cycle interpretation
3.6 comparative assertion
3.7 transparency
3.8 environmental aspect
3.9 product
3.10 co-product
3.11 process
3.12 elementary flow
3.13 energy flow
3.14 feedstock energy
3.15 raw material
  Definitions of all terms available at: https://www.iso.org/obp/ui/#iso:std:iso:14040:ed-2:v1:en
3.32 system boundary
3.33 uncertainty analysis
3.34 unit process
3.35 waste
3.36 category endpoint
3.37 characterization factor
3.38 environmental mechanism
3.39 impact category
3.40 impact category indicator
3.41 completeness check
3.42 consistency check
3.43 sensitivity check
3.44 evaluation
3.45 critical review
3.46 interested party
3.16 ancillary input
3.17 allocation
3.18 cut-off criteria
3.19 data quality
3.20 functional unit
3.21 input
3.22 intermediate flow
3.23 intermediate product
3.24 life cycle inventory analysis result
3.25 output
3.26 process energy
3.27 product flow
3.28 product system
3.29 reference flow
3.30 releases
3.31 sensitivity analysis

## Slide 19: Select Terms and Definitions in ISO 14040
Process
  Set of interrelated or interacting activities that transforms inputs into outputs
Elementary flow
  Material or energy entering the system being studied that has been drawn from the environment without previous human transformation, or material or energy leaving the system being studied that is released into the environment without subsequent human transformation
Product flow
  Products entering from or leaving to another product system
Intermediate flow
  Product, material or energy flow occurring between unit processes of the product system being studied
System boundary
  Set of criteria specifying which unit processes are part of a product system
Impact category
  Class representing environmental issues of concern to which life cycle inventory analysis results may be assigned
Characterization factor
  Factor derived from a characterization model which is applied to convert an assigned life cycle inventory analysis result to the common unit of the category indicator
Allocation
  Partitioning the input or output flows of a process or a product system between the product system under study and one or more other product systems
Additional details in alpha modules
All definitions directly quoted from ISO 14040:2006

## Slide 20: Thank you for completing Module A1!
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules

## Slide 21: Self-Assessment Quiz
MODULE A1: Introduction to Life Cycle Assessment and ISO 14040

## Slide 22: What does LCI stand for?
Life Cycle Introduction
Life Cycle Interpretation
Life Cycle Inventory

## Slide 23: Correct!
LCI stands for Life Cycle Inventory

## Slide 24: How many phases are there in an LCA?
4
6
8

## Slide 25: Correct!
The phases are:
Goal and Scope
Life Cycle Inventory
Life Cycle Impact Assessment
Interpretation

## Slide 26: What is one of the intended benefits of a critical review?
Improves credibility by showing adherence to the Standard
Validates goals and intended use of the results
Provides an endorsement of the product by the review panel
All of the above

## Slide 27: Correct!
The critical review can make the study more credible by demonstrating adherence to ISO 14040 and 14044, but does not endorse products or validate goals and intended uses of the LCA.

## Slide 28: Can the Goal and Scope be updated while completing the LCI stage?
No, it must be left as originally written
Yes, but it should be avoided if possible
Yes, this type of iterative process is encouraged and can strengthen results

## Slide 29: Correct!
The entire process of life cycle assessment is iterative between each phase to accommodate incorporation of new information at any point.

## Slide 30: What is the first priority of the scientific approach to characterizing impacts?
Social and economic science
Value choices
Natural science

## Slide 31: Correct!
Natural sciences tend to be more objective and therefore are the first priority in characterizing impacts.

## Slide 32: Sorry that’s Incorrect
Please try again!