## Slide 1: Welcome to the Life Cycle Assessment (LCA) Learning Module Series
Acknowledgements:
CESTiCC Washington State University Fulbright
Liv Haselbach Quinn Langfitt
For current modules email haselbach@wsu.edu or visit cem.uaf.edu/CESTiCC

## Slide 2: LCA Module Series Groups
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules

## Slide 3: System, System Boundary, and Allocation
Module α2
It is suggested to review Modules A1 and A2 prior to this module

## Slide 4: Processes
Fertilizer
Process
“Set of interrelated or interacting activities that transforms inputs into outputs.”*
Grow Corn
Seed
Water
Tilling
Corn
Fertilizer
Runoff
Produce Ethanol
Corn
Natural gas
Electricity
Enzymes
Ethanol
Stillage
Milling
Whole corn
Electricity
Corn flour
Unit process
“Smallest element considered in the life cycle inventory analysis for which input and output data are quantified.”*
Yeast
Carbon dioxide
Water
General Unit Process Diagram: Scott et al. 2013 *ISO 14040

## Slide 5: Product System
“Collection of unit processes with elementary and product flows, performing one or more defined functions, and which models the life cycle of a product”*
*ISO 14040 Diagram: Geyer, R., Kuczenski, B., Henderson, A., Zink, T. (2013). “Life Cycle Assessment of Used Oil Management in California.” California Dep. of Resources Recycling and Recovery.

## Slide 6: System Boundary
“Set of criteria specifying which unit processes are part of a product system”*
Ideally only materials and energy directly from and to the environment would cross boundary
  Practically inputs and outputs from other systems will cross
Choice of system boundary will affect results
Raw materials from environment
Energy
Materials to Environment
Energy
Ideal System Boundary
Raw materials from envr.
Energy
Materials to Environment
Energy
Practical System Boundary
Inputs from other systems
Outputs to other systems
System Boundary
System Boundary
Process A
Process A
Process B
*ISO 14040
Process B
Process C
Process D

## Slide 7: System Boundary - Corn Ethanol
Corn Grain
Fertilizer Production
Fertilizer
Pesticide Production
Pesticides
Diesel
Farm Infrastructure Manufacture
Diesel Production
Infrastr.
Water
Sunlight
Seed Production
Seeds
Farming Processes
Grain Processing
Ethanol Product.
Processes
Corn Stover
Ethanol
Prod. Equip. Manufacture
Equip.
Inputs to fertilizer, pesticide, seed, ethanol production
Ethanol Combustion
Energy
Emissions to air
Emissions to water
Emissions to soil
System Boundary
Inputs
Inputs
Inputs
Out
Out
Out
Inputs
Outputs

## Slide 8: Cut-off criteria
“Specification of the amount of material or energy flow or the level of environmental significance associated with unit processes or product system to be excluded from a study.”*
Why are they useful?
  Reduce omissions of important processes/flows
  Reduce data collection waste for inconsequential processes/flows
Can be based on mass, energy, or environmental significance
  Best to avoid mass-only cut-off criteria
Can be based on percentage of a process or percentage in overall system
If all flows from a process would fall below cut-off, whole process would be excluded
  For example: development of infrastructure and capital goods are generally excluded
Possible effects of cut-off criteria should be assessed and described
*ISO 14040

## Slide 9: Allocation
“Partitioning the input or output flows of a process or a product system between the product system under study and one or more other product systems.”*
Main cases:
  Co-products
  Reuse/recycling
Many choices to deal with partitioning
  Best one is to avoid allocation altogether
Must state procedures to use in the scope
Allocation procedures for similar scenarios within study should be consistent
*ISO 14040 Image source: tinleypark.org
Process
Product A
Product B

## Slide 10: Allocation Decision Tree (Simonen 2014)
Diagram: Simonen, K. (2014). Life Cycle Assessment. Routledge, New York, NY.
Must do sensitivity analysis

## Slide 11: Allocation – Co-products
Co-products: more than one product is produced in a single unit process
How much of the process impacts should be assigned to each product?
  Mass, volume, energy are common ways to decide based on physical relationships
No physical relationship between outputs
  Economic value is a common choice
Consider if one is waste or if they are truly co-products
Frequently encountered in following industries:
  Chemical
  Agricultural
  Mining
  Oil refining
  Metallurgy
Figure source: http://www.epa.gov/nrmrl/std/lca/pdfs/chapter3lca101.pdf

## Slide 12: System Expansion to Avoid Allocation
Figures adapted from: Klöpffer, W. and Grahl, B. (2014). Life Cycle Assessment (LCA). Wiley, Weinheim, Germany.
  By addition
Production Processes for A and B
Production Processes for B
x kg Product A
–
y kg Product B
y kg Product B
Inputs
Emissions/Wastes
System 1
=
x kg of Product A
Inputs
Emissions/Wastes
Production Processes for C
z kg Product C
Inputs
Emissions/Wastes
System 2
=
z kg of Product C
Production Processes for A and B
x kg Product A
+
y kg Product B
Inputs
Emissions/Wastes
System 1
=
x kg of Product A
+
y kg Product B
Production Processes for C
z kg Product C
Inputs
Emissions/Wastes
System 2
=
z kg of Product C
+
y kg Product B
  Output by system:
  x kg Product A
  z kg Product C
  Want to compare Products A and C
  By subtraction
Production Processes for B
y kg Product B
Emissions/Wastes
  Output by system:
  x kg Product A y kg Product B
  z kg Product C y kg Product B
Inputs

## Slide 13: Co-products – Corn Grain and Stover
Corn Grain
Fertilizer Production
Fertilizer
Pesticide Production
Pesticides
Diesel
Farm Infrastructure Manufacture
Diesel Production
Infrastr.
Water
Sunlight
Seed Production
Seeds
Farming Processes
Grain Processing
Ethanol Product.
Processes
Corn Stover
Ethanol
Prod. Equip. Manufacture
Equip.
Inputs to fertilizer, pesticide, seed, ethanol production
Ethanol Combustion
Energy
Emissions to air
Emissions to water
Emissions to soil
System Boundary
Inputs
Inputs
Inputs
Out
Out
Out
Inputs
Outputs

## Slide 14: Allocation – Reuse/Recycling
Two things happening
  Impacts from recycling/reuse process
  Impacts avoided from using recycled material rather primary (similar to subtractive system expansion)
Question: Which product takes on these impacts/avoided impacts?
  The one being disposed of?
  The one being produced?
Examples:
  Aluminum recycling
  Lube oil re-refining
  Tire burning for energy recovery
Consider if properties of product are different than from production with primary materials

## Slide 15: Allocation – Reuse/Recycling
Crude oil
Produce base oil
Blend additives
Use oil
Recycle oil into base oil
Recycle into MDO
Crude oil
Produce MDO
Use fuel
Closed Loop Recycling
Open Loop Recycling
Lubricating Oil
Marine Diesel Oil (fuel)

## Slide 16: Allocation – Reuse/Recycling
Closed loop – relatively simple
Open loop – more difficult allocation decision
With open loop, less MDO from crude oil needed so can discount impacts, but from where:
  End-of-life method: from lube oil life– rewards recyclable products
  Recycled content method: from MDO life cycle – reward products made from recycled materials
  Equal parts: half to lube oil, half to MDO
  Decide that certain recycling processes go with one system and others to the other

## Slide 17: Allocation – Reuse/Recycling – Open Loop
  Reward allocated to lubricating oil in this example for lube oil disposal (End-of life method)
Figure source: Langfitt, Q., and Haselbach L. (2014). “Assessment of Lube Oil Management and Self-Cleaning Oil Filer Feasibility in WSF Vessels.” Report for PacTrans.

## Slide 18: Thank you for completing Module α2!
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules

## Slide 19: Homework
Draw a simple system diagram for generation of electricity in a coal fired power plant. Look up online what some of the major inputs, outputs, and processes are (detailed inputs and outputs are available from the US LCI website if interested). Don’t worry about capturing all of the flows and processes, just draw a simplified diagram with a few majors ones. Be sure to include a system boundary and place a process for use of the electricity outside of this boundary.
Find an LCA study that addresses cutoff criteria and write the authors names, year, and title of the study. What did they use for their criteria?
Describe the two ways in which allocation can be avoided for systems with co-products.
Describe the difference between a closed loop and an open loop recycling process. Give an example of each besides the lubricating oil example given in this module.