## Slide 1: Welcome to the Life Cycle Assessment (LCA) Learning Module Series
Acknowledgements:
CESTiCC Washington State University Fulbright
Liv Haselbach Quinn Langfitt
For current modules email haselbach@wsu.edu or visit cem.uaf.edu/CESTiCC

## Slide 2: LCA Module Series Groups
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules

## Slide 3: Life Cycle Stages
Module α3

## Slide 4: Phases versus Stages
Inventory Analysis
Impact Assessment
Goal and Scope
Interpretation
Phases
  Portions of LCA procedure
Figure: ISO 14040:2006
Stages
  Sections of product life cycle
Manufacture
Disposal/recycling
Extraction and upstream production
Transport
Use
Transport
Transport
  Note: This is a general diagram of stages and some products or processes may have more or less stages than those shown here

## Slide 5: Life Cycle of a Building
Source (bottom cropped): WBCSD Cement Sustainability Initiative, PCR for concrete, UN CPC 375, 2013-02-12

## Slide 6: Life Cycle Split by Stages Analyzed
Source: WBCSD Cement Sustainability Initiative, PCR for concrete, UN CPC 375, 2013-02-12
Most common/applicable to wide range of situations

## Slide 7: Life Cycle of a Transportation Fuel
Image Source (without dashed boxes): transportblog.co.nz
Well-to-Pump
Pump-to-Wheel
Well-to-Wheel

## Slide 8: Inputs and Outputs throughout Stages
Source: Environmental Protection Agency. 1993. Life Cycle Assessment: Inventory Guidelines and Principles. EPA/600/R-92/245. Office of Research and Development. Cincinnati, Ohio, USA.

## Slide 9: Why Split into Stages?
Organize data collection
Organize presentation
Identify weak environmental links in life cycle
Group unit processes to make it easier to identify which were included
Allow for easier aggregation and disaggregation
  For others studying the product with only one or two stages different
  For ability to consider cradle-to-gate instead of cradle-to-grave only

## Slide 10: Software Organizing by Life Cycle Stage
Quantis screenshot: Quantis (2013). “QS Product Free 2 project and system setup” YouTube, https://www.youtube.com/watch?v=utUd4hE-ZVw

## Slide 11: Common Stages (Covered in this Module)
Raw Materials/Upstream Processing
Manufacture
Use
Disposal/Recycling/Reuse
*Other stages, such as construction (execution), could be included depending on the product/system
Transportation
Transportation
Transportation

## Slide 12: Material Extraction/Upstream Processing
Material Extraction
Exploration for and removal of raw materials from natural systems
Image sources: phoenixparts.com, blog.tradequip.com, columbiatechnologies.com
Upstream processing
Transformation of raw materials into a form useful for manufacturing
  Equipment
  Fuel use
  Land use
  Water use
  Waste flows
  Some Considerations

## Slide 13: Manufacture
Transforming energy and raw/pre-processed materials into products, and packaging them for distribution
Image sources: madeintheusa.dreamlandinteractive.com angus-selfstorage.co.uk info.zentech.com
  Energy use (gas, electric, etc.)
  Raw material use
  Chemical use and wastes
  Equipment
  Co-products?
  Some Considerations
May include assembly of parts, transportation between facilities, packaging for distribution, and any uses and emissions from the facility

## Slide 14: Use
Consumer’s use of the product, including maintenance
Image source: livestrong.com
  How is the product intended to be used?
  How much will the product typically be used?
  What variations are possible (operating, environmental, etc.)?
  How much of the product might be spilled or improperly used?
  Some
  Considerations
Difficult to quantify in some cases since use can vary considerably and be out of the control of the company producing the product
  For example, use impacts from a lawn mower depends on
    Frequency of mowing
    Size of lawn
    Mower life span given treatment by user
    Quality of lubrication and other parts upkeep
Due to uncertainty, may be wise to examine multiple use cases

## Slide 15: Examples of products with varying levels of use impacts
Ruler
Few or no inputs or outputs during use
Acoustic guitar
Very infrequent, minor inputs/outputs
New strings
Old strings
Television
Regular energy input
Electricity
Car
Many frequent energy and material inputs/outputs
Gasoline
Oil/coolant/brake/washer fluids
Seals/replacement parts
Tailpipe emissions
Brake pads, tires
Oil/coolant leaks
Tire/brake wear
Dishwasher
A few frequent inputs/outputs
Electricity
Soap
Water
Wastewater
Used tires

## Slide 16: Disposal/Recycling/Reuse
Getting rid of product at the end of its life
Image source: theparkcatalog.com
Similar issues as use for uncertainty
  For example, disposal of lubricating oil could be done by
    Dumping (illegal)
    Incineration
    Re-refining
    Distillation
Due to uncertainty, may be wise to include multiple use cases in analysis or present sensitivity analyses
If recycling or reusing, some impacts may be offset in this stage
  Can sometimes result in net environmental benefits for this stage
  Example: -5 kg CO2-eq for GWP means that it was as if 5 kg of CO2 were sequestered (does not mean actual physical sequestration occurred)
  What disposal options possible?
  Which most likely?
  Is a product offset by disposal?
  Is there additional transport involved in this stage?
  Some Considerations

## Slide 17: Example of Disposal Routes for a Plastic Water Bottle
Plastic water bottle production from raw materials
Labeling, packaging, distribution
Use
Recycling of plastic and reforming into water bottles
Throw in recycle bin
Throw in trash
Refill with tap water and reuse
Disposal
Options

## Slide 18: Transport
Materials and products must be moved at multiple points in the life cycle
  After extraction
  After processing and/or manufacture
  To the customer
  To the disposal facility
Impacts from various transport methods are generally well studied
  Most databases have these processes
  Many studies in the literature
  Often only include energy, regulated emissions, and greenhouse gases
  Modes of transport
  Fuel type
  Distance
  Weight
  Shipped with other products?
  Some Considerations
Transport processes can be:
  Considered to be one stage overall
  Considered to be individual stages for each transport process
  Included as part of the stage directly before or after
    Choose one or the other to avoid double counting

## Slide 19: Common Transport Modes
Image sources: popularmechanics.com blog.uship.com truckstars.com maritime-connector.com jsg.utexas.edu boluo-logistics.com

## Slide 20: Thank you for completing Module α3!
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules

## Slide 21: Homework
For an LCA from the literature, write down which stages were included and whether or not data were presented separately for each stage. Cite the source of the LCA.
Find an example of a cradle-to-gate LCA. Did the authors give a reason for only including these stages, and if so what was it? What other considerations might have been important for comparing the products/processes during the use, disposal, or other stages?
Write an example for each of the levels of use impacts (as shown in slide 15) for components of highway systems or buildings:
  Little or no inputs or outputs
  Very infrequent/minor inputs and outputs
  Regular energy inputs, but little or no other inputs and outputs
  A few frequent inputs and outputs
  Many frequent inputs and outputs