## Slide 1: Welcome to the Life Cycle Assessment (LCA) Learning Module Series
Acknowledgements:
CESTiCC Washington State University Fulbright
Liv Haselbach Quinn Langfitt
For current modules email haselbach@wsu.edu or visit cem.uaf.edu/CESTiCC

## Slide 2: LCA Module Series Groups
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules

## Slide 3: Introduction to Impact Categories
Module B1
Additional acknowledgements to Trace Sendele
It is suggested to review Modules A1 and A2 prior to this module

## Slide 4: What is an Environmental Impact Category?
    “Class representing environmental issues of concern to which life cycle inventory analysis results may be assigned”*
Impact Category
    More simply:
    Types of environmental issues that could be caused by the inputs and outputs of the product or process being analyzed
*ISO 14040:2006
04/2015

## Slide 5: Classes of Impact Categories
Human Health
Ecosystems
Resources

## Slide 6: Common Emissions Impact Categories
Acidification Potential (AP)
Ecotoxicity Potential (ETP)
Eutrophication Potential (EP) (Also: Nutrification)
Global Warming Potential (GWP) (Also: Climate Change)
Human Toxicity Cancer Potential (HTCP) (Also: Human Health Cancer)
Human Toxicity Non-Cancer Potential (HTNCP) (Also: Human Health Non-Cancer)
Human Health Criteria Air Potential (HHCAP) (Also: Human Health Particulates)
Stratospheric Ozone Depletion Potential (OPD) (Also: Ozone Layer Depletion)
Smog Creation Potential (SCP) (Also: Photochemical Ozone Creation)
Some can be partitioned further into:
Air
Water
Soil
Module
B2
Module
B3

## Slide 7: Other impact categories
  (Ionizing) Radiation Potential
  Ecosystem Damage Potential
  Abiotic Resource Depletion Potential
  Biotic Resource Depletion Potential
  Fossil Fuel Depletion Potential
  Energy Use
  Land Use
  Water Use
  Landfill Use
  Nuisance-related Impacts (odor, sound, etc.)
  Indoor Air Quality
Particularly uncommon

## Slide 8
Process of Computing Environmental Impacts
Mandatory Elements
Classification
Impact category selection (Comprehensive set)
Characterization
Characterization model selection (impact methodology)
Category indicator selection

## Slide 9
Impact category selection:
  GWP, AP, EP, ETP, HTNCP, HTCP, HHCAP, ODP, SCP
Category indicator selection:
  kg CO2-eq for GWP, kg SO2-eq for AP, kg N-eq for EP, etc…
Characterization model selection:
  TRACI 2.1* (other options include IMPACT 2002+, eco-indicator 99, CML 2001…)
Classification:
  NH3 (Ammonia)  Acidification, Human Health Criteria Air, Eutrophication
Characterization:
  Acidification:
  Criteria air:
  Eutrophication:
Example of Process
Repeat for each flow, sum results in each impact category
Characterization factor
*TRACI is the Tool for the Reduction and Assessment of Chemical and Other Environmental Impacts

## Slide 10: Variability of Effects by Various Substances
Different substances force different amounts of impacts per unit mass
  1 kg NOx forces only 0.7 times the acidification potential as 1 kg SO2
Some emissions have different residence times in the atmosphere over which they force impacts
  Mostly applied to global warming potential
_
1 kg CO2
1 kg CH4
_
1 kg CO2
_
1 kg CH4
Mass Scale
“GWP” Scale
1 kg of substance | GWP* (CO2-eq)
Carbon Dioxide | 1
Carbon Tetrachloride | 1400
CFC 12 | 10,900
Chloroform | 31
Methane | 25
Methyl Bromide | 5
Nitrous Oxide | 298
1,1,1-Trichloroethane | 146
*Table of GWP values is a sample of substances using TRACI 2.1 methodology
100-Year Global Warming Potential

## Slide 11: Anthropogenic vs. Natural Sources
Natural sources of environmental impacts exist
  Volcanos emit SO2 (contributes to acidification)
  Respiration of organisms emits CO2
  Forests emit volatile organic compounds (can contribute to smog formation)
Life cycle assessment is not meant to quantify natural sources, but rather to guide process and product production that add additional emissions
  Therefore, only anthropogenic emissions are included in LCA
Anthropogenic
Caused by human activity
Image source: esrl.noaa.gov

## Slide 12: Geographic Breadth of Impacts
Global
Regional
Local
Global warming, ozone depletion, human toxicity
Acidification, eutrophication, human toxicity, water use
Acidification, eutrophication, smog, human toxicity
Images: Global: wikimedia.org U.S.: alg.umbc.edu Pin: cdn2.hubspot.net

## Slide 13: Impact Category Indicator
“Quantifiable representation of an impact category”*
*ISO 14040:2006
Global warming potential
25 kg CO2-eq
Acidification potential
5.4 kg SO2-eq or 274 moles H+-eq
Ozone layer depletion
Photochemical oxidation (Ex. Smog)
4.9 kg CFC-11 eq
1.2 kg C2H4-eq or 10.8 kg O3-eq

## Slide 14: Types of Impact Category Indicators
Adapted from: Bare, J., Norris, G., Pennington, D., and McKone, T. (2002). “Traci.” Journal of Industrial Ecology, 6(3‐4), 49-78.
Emissions of ozone depleting substances
Substances are transported to stratosphere where Cl- and Br- detach
Ozone depleted based on substance’s reactivity/lifetime
Reduced ozone allows increased UVB penetration
Effects on human health, plants, organisms buildings, etc.
Midpoint
  Direct effects
  Objective
Endpoint
  Final effects
  Interpretable
Examples of Endpoints:
Skin cancer
Cataracts
Damage to:
Crops
Materials
Marine Life
Immune system
Example of Midpoint:
Releases of all substances equal in ozone depletion to x kg CFC-11
Ozone Depletion Flow Diagram

## Slide 15: Impacts are “Potential”
*ISO 14040:2006
    Various limitations lead to the necessity to call environmental impacts identified in LCA “potentials”:
    Underlying simplifications
    Underlying assumptions
    Lack of resolution:
      Pollutant release of a certain quantity into a small stream may be worse than a large river
      Large release of substance in a short time period would have different impacts than over a long time period
      Release of nitrogen into a phosphorus-limited environment will not contribute significantly to eutrophication
        Phosphorus-limited means there is already an abundance of nitrogen present, but little phosphorus
    Linear models for characterization
    Imperfect characterization factors for other reasons
*assumptions and simplifications need to be reviewed after study

## Slide 16: Thank you for completing Module B1!
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules

## Slide 17: Self-Assessment Quiz
MODULE B1: Introduction to impact categories

## Slide 18: Which of these is not an overall class of environmental impact categories in LCA?
Human Health Impacts
Ecosystem Impacts
  Natural Resource Impacts
  Built Environment Impacts

## Slide 19: Correct!
While some the endpoints of the impact categories do include the built environment, it is not a focus in LCA or of any impact category and is not an overall class, at least in our interpretation.

## Slide 20: Which impact category has a global geographic breadth?
Human Toxicity Potential
Photochemical Smog Potential
Eutrophication Potential

## Slide 21: Correct!
Human toxicity (human health) can have global, regional, or local effects depending on transport of the substances which cause those impacts.

## Slide 22: Which of these is a common category indicator for acidification potential?
kg SO2-equivalent
kg CFC-11-eqivalent
kg CO2-eqivalent
kg C2H4-equivalent

## Slide 23: Correct!
kg SO2-eq is commonly used for acidification potential

## Slide 24: Which would be more likely to have acute impacts on human health (may not be captured in LCA)?
10 tons of particulate material released in a one week period
10 tons of particulate material released in a one year period
They are equivalent

## Slide 25: Correct!
Releasing 10 tons of particulate matter in a one week span is more likely to have significant acute impacts on human health than releasing 10 tons over a year because the first scenario might lead to higher concentrations.

## Slide 26: Which of these would be considered a midpoint for global warming potential?
Changes in wind and ocean currents
Increased radiative forcing
Sea level rise

## Slide 27: Correct!
Increased radiative forcing is the direct result of increases in greenhouse gas concentrations (the midpoint), whereas issues like sea level rise and changes in wind and ocean currents would be considered endpoints.

## Slide 28: Sorry that’s Incorrect
Please try again!