## Slide 1: Welcome to the Life Cycle Assessment (LCA) Learning Module Series
Acknowledgements:
CESTiCC Washington State University Fulbright
Liv Haselbach Quinn Langfitt
For current modules email haselbach@wsu.edu or visit cem.uaf.edu/CESTiCC

## Slide 2: LCA Module Series Groups
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules

## Slide 3: Common Air Emission Impact Categories
Module B2
Additional acknowledgements to Trace Sendele
It is suggested to review Modules B1 prior to this module

## Slide 4: Summary of Module B1 and Other Points
All impacts are “potential”
Only anthropogenic sources are included
Different substances have different relative amounts of forcing
  Usually results are related to the equivalent release of a particular substance
Different impact categories have different scales of impacts
  Global, regional, local
Ryberg, M., Vieira, M.D.M., Zgola, M., Bare, J., and Rosenbaum, R.K. (2014). “Updated US and Canadian normalization factors for TRACI 2.1.” Clean Technology and Environmental Policy, 16(2), 329-339.
Watch Module B1 for background
β modules for more details
Percentages of impact contributed by various substances is based on total US inventory from Ryberg et al. 2014 and represents the percentage of impacts, not the mass percentage
More impact categories are available than can be covered in this module series

## Slide 5: Common Impact Categories
Acidification Potential (AP)
Global Warming/Climate Change Potential (GWP)
Smog/Ozone/Photochemical Oxidants/Creation Potential (SCP)
Stratospheric Ozone Depletion Potential (ODP)
Human Health Particulates/Criteria Air Potential (HHCAP)
Human Health/Toxicity Cancer/Non-Cancer Potential (HTP)
Ecotoxicity Potential (ETP)
Eutrophication Potential (EP)
Air
Air
Water
Soil
Bolded impact categories are those covered in this module
These are only some of the possible impact categories in LCA

## Slide 6: Some Other Impact Categories
Radiation
Abiotic resource depletion
Fossil fuel depletion
Biotic resource depletion
Energy demand
Water use
Land use
Nuisance-related (noise, odor, etc.)
Indoor air quality

## Slide 7: Acidification Potential (AP)
Emissions which increase acidity (lower pH) of water and soils
  Most common form of deposition is as acid rain
  Dry and cloud deposition also occur
  Ocean acidification from CO2 not included
Only anthropogenic sources are included, though natural sources exist too (such as volcanoes)
Regional variations can be important
Commonly reported as:
  kg SO2-eq
  mol H+-eq
Image source: blog.epa.gov
Local
Regional
Scale of impacts:
SO2: sulfur dioxide mol: ~6*1023 atoms H+: hydrogen ion

## Slide 8: Acidification Potential (AP)
*Ryberg et al. 2014 Building damage: h2owash.biz Forest: Britannica.com Power plant: ehow.com
Plants (esp. forests)
Organisms
NOx
Main substances*
Increased soil and water acidity
Midpoint
Fuel combustion
Electricity
Major sources
Agriculture
38%
SOx
35%
NH3
26%
Others: 1%
Buildings
Possible Endpoints
Transportation
NOx: nitrogen oxides SOx: sulfur oxides NH3: ammonia

## Slide 9: Global Warming Potential (GWP)
Increase in greenhouse gas concentrations, resulting in potential increases in global average surface temperature
  Occurs due to the greenhouse effect
  Often called climate change to reflect scope of possible effects
  CO2 is biggest anthropogenic source, other sources too
Some greenhouse effect necessary, additional forced by humans is what is counted in LCA
Biogenic CO2 may or may not be counted
  e.g. biofuels
GWP typically reported as 100 year time scale
Almost universally reported as kg CO2-equivalent
Source: livescience.com
Global
Scale of impacts:
CO2: carbon dioxide

## Slide 10: Global Warming Potential (GWP)
*Ryberg et al. 2014 CO2 plot: Wikimedia.org Glacier: nrmsc.usgs.gov
Increase in severe weather frequency
Sea level increase
CO2
Main substances*
Increased radiative forcing (trapping heat)
Midpoint
Fuel combustion
Electricity
Major sources
Agriculture
80%
CH4
9%
N2O, O3, H2O(g), CFCs, Others
Increase in heat-related illnesses
Possible Endpoints
Transportation
Industrial processes
11%
Wind and ocean current changes
Soil moisture loss
CO2: carbon dioxide CH4: methane N2O: nitrous oxide O3: ozone H2O(g): water vapor CFC: chlorofluorocarbons

## Slide 11: Ozone
Ozone molecule: naturallythebest.com Good/bad ozone: epa.gov
Molecule composed of three oxygen atoms
Colorless, odorless gas
The focus of two very different impact categories
  Ozone depletion potential – “Good” ozone
  Smog creation potential – “Bad” ozone

## Slide 12: Ozone Depletion Potential (ODP)
Reduction of ozone concentration in the stratosphere
  This is “good” ozone which filters out UV-B radiation
  Additional UV can cause skin cancer, crop damage, material damage
  Primarily caused when CFCs and halons lose chlorine and bromine atoms in reaction with sunlight and catalyzes ozone decomposition reactions
  Not a major cause of climate change
Ozone depletion less prevalent since Montreal Protocol (1987)
  Required replacement of CFCs with other compounds
  Reduction of 98% in ODP emissions since then
  Still important to consider, especially for particular sectors
Almost universally reported as kg CFC-11-equivalent
  Previously common refrigerant
Image source: epa.gov
Global
Scale of impacts:
CFCs: chlorofluorocarbons

## Slide 13: Ozone Depletion Potential (ODP)
Skin cancer
Halon 1301
Main substances*
Decrease in stratospheric ozone concentration
Midpoint
Manufacturing (polymers, aerosols)
Major sources
Refrigerant systems
29%
CFC-11
22%
Others: 26%
Possible Endpoints (Due to increased UV-B radiation)
Fire extinguishers
Crop damage
*Ryberg et al. 2014 Ozone hole: Wikipedia.org Ozone chemistry: environmental-chemistry.wikispaces.com
Materials damage
Marine life damage
CFC-12
14%
HCFC-22
9%
CFC: chlorofluorocarbon HCFC: hydrochlorofluorocarbon

## Slide 14: Smog Creation Potential (SCP)
Increased formation of ground level ozone
  Also called photoxidant formation, ozone creation, etc.
  Formed from reactions of NOx, VOCs, other pollutants, and sunlight
  Can have effects on human health and vegetation
Effects vary, but LCA does not usually capture, based on:
  Current air composition (i.e. NOx or VOC limited)
  Time of day and year (sunlight)
  Physical characteristics of area and weather patterns
  Exposed populations
Commonly expressed as:
  kg O3-equivalent
  kg C2H4-equivalent
  kg NOx-equivalent
Image source: edmunds.com
Scale of impacts:
Local
O3: ozone C2H4: ethane NOx: nitrogen oxides VOCs: volatile organic compounds

## Slide 15: Smog Creation Potential (SCP)
Reduced lung function/aggravation
NOx
Main substances*
Increase in ground-level
ozone concentration
Midpoint
Cars and other vehicles
Major sources
Energy production
87%
VOCs
11%
Others: 2%
Possible Endpoints
Industrial processes
Aggravate Asthma
*Ryberg et al. 2014 Image source: science.nature.nps.gov
Vegetation damage
Eye irritation
NOx: nitrogen oxides VOCs: volatile organic compounds
2005-2009 4th highest annual value of maximum daily 8-hr. ozone in ppb

## Slide 16: Common Impact Categories
Acidification Potential (AP)
Global Warming/Climate Change Potential (GWP)
Smog/Ozone/Photochemical Oxidants/Creation Potential (SCP)
Stratospheric Ozone Depletion Potential (ODP)
Human Health Particulates/Criteria Air Potential (HHCAP)
Human Health/Toxicity Cancer/Non-Cancer Potential (HTP)
Ecotoxicity Potential (ETP)
Eutrophication Potential (EP)
Air
Air
Water
Soil

## Slide 17: Thank you for completing Module B2!
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules

## Slide 18: Self-Assessment Quiz
MODULE B2: Common Air Emission Impact Categories

## Slide 19: What is the most common form of deposition for acidification potential?
Dry deposition
Acid rain
Ocean acidification from CO2

## Slide 20: Correct!
Acid rain is the most common way that acidifying substances are deposited in the acidification potential category. Dry deposition happens less often, and ocean acidification by CO2 is not included in that category.

## Slide 21: What time scale is most often used for determining global warming potential in LCA?
1 year
50 year
100 year

## Slide 22: Correct!
Global warming potential is usually characterized based on a 100 year time scale, though other time scales like 50 year and 500 year are occasionally used.

## Slide 23: Which type of ozone is considered “good”?
Tropospheric
Both
Stratospheric
Neither

## Slide 24: Correct!
Ozone in the stratosphere (high up) filters UV-B radiation, while ozone in the troposphere (near ground) can be a health a hazard when breathed in.

## Slide 25: What is the main direct result of decreased ozone concentrations in the stratosphere?
More ground-level ozone mixes up into the stratosphere to create an equilibrium reducing smog
More UV-B radiation reaches Earth’s surface resulting in impacts such as higher rates of skin cancer, crop damage, and building damage
Increased greenhouse gas effect contributing to global warming

## Slide 26: Correct!
Ozone depletion in the stratosphere allows more UV-B radiation to penetrate the atmosphere. It does not significantly affect global warming or interactions with ground-level ozone.

## Slide 27: How is ground level ozone (smog) most commonly formed?
Reactions of NOx and VOCs in the presence of sunlight
Reactions with oxygen catalyzed by chlorine atoms from CFCs and halons
Directly emitted from combustion of fossil fuels

## Slide 28: Correct!
Ground level ozone is mostly formed in reaction cycles of NOx and VOCs in the presence of sunlight. Chlorine catalyzed reactions from CFCs and halons are the main contributors of stratospheric ozone depletion, and ozone is rarely emitted directly from any sources.

## Slide 29: Sorry that’s Incorrect
Please try again!