## Slide 1: Welcome to the Life Cycle Assessment (LCA) Learning Module Series
Acknowledgements:
CESTiCC Washington State University Fulbright
Liv Haselbach Quinn Langfitt
For current modules email haselbach@wsu.edu or visit cem.uaf.edu/CESTiCC

## Slide 2: LCA Module Series Groups
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules

## Slide 3: Other Common Emissions Impact Categories
Module B3

## Slide 4: Summary of Module B1 and Other Points
All impacts are “potential”
Only anthropogenic sources are included
Different substances have different relative amounts of forcing
  Usually results are related to the equivalent release of a particular substance
Different impact categories have different scales of impacts
  Global, regional, local
Ryberg, M., Vieira, M.D.M., Zgola, M., Bare, J., and Rosenbaum, R.K. (2014). “Updated US and Canadian normalization factors for TRACI 2.1.” Clean Technology and Environmental Policy, 16(2), 329-339.
Watch Module B1 for background
β modules for more details
Percentages of impact contributed by various substances is based on total US inventory from Ryberg et al. 2014 and represents the percentage of impacts, not the mass percentage
More impact categories are available than can be covered in this module series

## Slide 5: Common Impact Categories
Acidification Potential (AP)
Global Warming/Climate Change Potential (GWP)
Smog/Ozone/Photochemical Oxidants/Creation Potential (SCP)
Stratospheric Ozone Depletion Potential (ODP)
Human Health Particulates/Criteria Air Potential (HHCAP)
Human Health/Toxicity Cancer/Non-Cancer Potential (HTP)
Ecotoxicity Potential (ETP)
Eutrophication Potential (EP)
Air
Air
Water
Soil
Bolded impact categories are those covered in this module
These are only some of the possible impact categories in LCA

## Slide 6: Some Other Impact Categories
Radiation
Abiotic resource depletion
Fossil fuel depletion
Biotic resource depletion
Energy demand
Water use
Land use
Nuisance-related (noise, odor, etc.)
Indoor air quality

## Slide 7: Eutrophication Potential
Excessive biological activity of organisms due to over-nutrification
  Especially in aquatic systems, often apparent through algal blooms
  Can lead to oxygen deficiency in water killing aquatic life
  Mostly forced by nitrogen and phosphorus
  Also called nutrification
Organisms need nutrients to grow, but too much can have undesirable consequences
Local variations can be very important
Commonly reported as:
  kg PO43- -equivalent (phosphate)
  kg P-equivalent (phosphorus)
  kg NO3—equivalent (nitrate)
  kg N-equivalent (nitrogen)
Source: ecodetail.net.au
Scale of impacts:
esp. in
fresh water
esp. in salt
water and soil
Local

## Slide 8: Eutrophication Potential
Algal bloom: apporpedia.org
Loss of biodiversity
Death of aquatic life
Nitrogen
Main substances
Excessive biological growth, especially of algae
Midpoint
Fossil fuel Combustion
Major sources
Storm and wastewater
42%
Phosphorus
33%
NH3
7%
Others: 8%
Foul odor
Possible Endpoints (mostly due to aquatic oxygen depletion)
Agricultural runoff
Septic field seepage
Water
NOx
10%
Air
esp. freshwater
esp. marine

## Slide 9: Human Toxicity Potential
Effects to individual human health that can lead to disease or death
  Usually split between carcinogenic and non-carcinogenic
  Can either cause or aggravate existing health conditions
  Only considers direct impacts, indirect ones in other impact categories
  Large scale impacts, not facility specific (occupational) ones
  Organic chemicals and metals are some of the largest contributors
Much uncertainty in characterization factors
  No true midpoint to consider
  Based on linear models, but toxicity effects are usually non-linear
Characterization commonly done through USEtox factors
  Considers fate, exposure, and effect factors
Commonly expressed as:
  kg benzene-eq (cancer) or kg toluene-eq (non-cancer)
  Cases (also called Comparative Toxicity Unit – CTU)
Source: NIH Medical Arts and Printing
Scale of impacts:
Local
Global
Regional

## Slide 10: Human Toxicity Potential
Image source: globalhealingcenter.com
Heart disease
Asthma
Zinc
Some major substances
General health effects on humans (no true midpoint)
Midpoint
Mining
Major sources
Energy production
Arsenic
Low birth rate
Possible Endpoints (either causing or aggravating)
Manufacturing
Cancer
Chromium
6%
Formaldehyde
Dioxins
Benzo(a)pyrene
Agriculture

## Slide 11: Ecotoxicity Potential
Impacts on whole ecosystems that can decrease production and/or decrease biodiversity
  More focused on whole system impacts than individual impacts
  Sometimes split between aquatic (water) and terrestrial (soil)
  Mostly forced by emissions of metals and organic chemicals
Characterization commonly done through USEtox factors
  Considers fate, exposure, and effect factors
Much uncertainty in characterization factors
  No true midpoint
  Factors based on only a few species, but wider ecosystem effects more difficult to deduce
Commonly expressed as:
  kg 2,4-dichlorophenoxy-acetic acid (2,4-D) - equivalent
  Potentially affected fraction (PAF) (also called Comparative Toxicity Unit – CTU)
Image source: scienceinthebox.com (P&G website)
Scale of impacts:
Local

## Slide 12: Ecotoxicity Potential
Image source: dosits.org
Decreased populations
Zinc
Main substances
General degradation of ecosystems (no true midpoint)
Midpoint
Copper
Possible Endpoints
Decreased biodiversity
Organic Chemicals
Mining
Major sources
Energy production
Manufacturing
Agriculture

## Slide 13: Human Health – Particulates
Health issues related to increased respiration of very small particles
  Small particles released directly and formed through secondary reactions
  When breathed into lungs may cause respiratory disease and cancer
  Category also called “criteria air pollutants”, but really only deals with subset
Health issues more severe for higher risk individuals
  Children, elderly, those with asthma
Usually midpoint quantified as:
  kg PM2.5-eq
  kg PM10-eq
Sometimes reported more as endpoint:
  Disability adjusted life years (DALYs)
Image source: epa.gov
Scale of impacts:
Local
Global
Regional

## Slide 14: Human Health – Particulates
Heart health effects
PM10
Main substances
Increased human exposure to particulate matter
Midpoint
Fossil fuel combustion
Major sources
Dust from roads
44%
PM2.5
43%
Possible Endpoints
Wood burning
Image source: bcairquality.ca
Aggravated asthma
Decreased lung function
SOx
8%
NOx and Others
5%
Dust from fields
Cancer

## Slide 15: A Couple More
Radiation: Regular releases of radioactive material which can have carcinogenetic and hereditary effects
Abiotic resource depletion: Uses of minerals, ores, etc. based on relative scarcity and overall consumption
Fossil fuel depletion: Similar to abiotic resources except based on energy content, not mass
Biotic resource depletion: Uses of recently living materials based on use rate, formation rate, and reserves
Energy demand: Energy required of all stages of life cycle (not energy content)
  Embodied energy is a subset of energy demand for only life cycle stages involved in producing the product
Water use: Typically just an inventory of fresh water use, sometimes differentiated by quality
Land use: Alteration to habitats, particularly for threatened and endangered species
Nuisance-related (noise, odor, etc.): Reduced quality of life for humans due to nuisance (rarely included in LCA)
Indoor air quality: Human health impacts of indoor air pollutants, especially VOCs (rarely included in LCA)

## Slide 16: Thank you for completing Module B3!
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules

## Slide 17: Self-Assessment Quiz
MODULE B3: other common emission impact categories

## Slide 18: By what mechanism does eutrophication usually cause the most damage to aquatic life?
Algae blooms deplete the water of oxygen leaving little for other organisms
Toxic levels of nutrients kill aquatic life when they uptake too much
Algae blooms block sunlight causing temperatures to drop in the water

## Slide 19: Correct!
The main way in which eutrophication impacts manifest themselves is through excessive growth of algae depleting the water of oxygen and leaving too little for many other organisms to survive.

## Slide 20: Which of these is not included as a factor in USEtox characterization of human toxicity?
Fate (transport of toxic chemicals)
Effects (toxicity in humans)
Exposure (intake by humans)
Interactions (effects of chemicals in combination with one another)

## Slide 21: Correct!
While interactions of chemicals may have an impact on their effects, characterization is done separately for each substance so interactions are not considered. Fate, exposure, and effects are the three factors used.

## Slide 22: The human toxicity impact category is often split into which of the following classifications?
Cancer and non-cancer effects
Acute and chronic effects
Nervous system, circulatory system, and respiratory system effects

## Slide 23: Correct!
Human toxicity is frequently differentiated into two separate impact categories: human cancer toxicity and human non-cancer toxicity.

## Slide 24: Besides animals vs. humans, what is the major conceptual difference between human toxicity and ecotoxicity?
Human toxicity uses non-linear dose-effects relationships while ecotoxicity uses linear ones
Human toxicity is more focused on the health of each individual, while ecotoxicity is more focused on overall ecosystem impacts
Human toxicity is focused on acute effects, but ecotoxicity on chronic effects

## Slide 25: Correct!
Human toxicity is focused on health issues of the individual, but ecotoxicity attempts to focus on overall ecosystem impacts, and not so much on health issues on individual organisms (at least in conception – these are complex considerations).

## Slide 26: How can anthropogenic particulate matter get into the air?
Directly released as particulate matter (from combustion, physical processes, etc.)
Formed in the atmosphere from gaseous emissions reactions
Both of the above

## Slide 27: Correct!
Particulate matter can be directly emitted from chemical and physical processes, or be formed secondarily in the atmosphere from reactions of gases such as NOx, SOx, and VOCs.

## Slide 28: Sorry that’s Incorrect
Please try again!