## Slide 1: Welcome to the Life Cycle Assessment (LCA) Learning Module Series
Acknowledgements:
CESTiCC Washington State University Fulbright
Liv Haselbach Quinn Langfitt
For current modules email haselbach@wsu.edu or visit cem.uaf.edu/CESTiCC

## Slide 2: LCA Module Series Groups
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules

## Slide 3: Global Warming Potential (GWP)
Module β1
It is suggested to review Modules B1 and B2 prior to this module

## Slide 4: Summary of Module B1 and Other Points
All impacts are “potential”
Only anthropogenic sources are included
Different substances have different relative amounts of forcing
  Usually results are related to the equivalent release of a particular substance
Different impact categories have different scales of impacts
  Global, regional, local
Ryberg, M., Vieira, M.D.M., Zgola, M., Bare, J., and Rosenbaum, R.K. (2014). “Updated US and Canadian normalization factors for TRACI 2.1.” Clean Technology and Environmental Policy, 16(2), 329-339.
Watch Module B1 for background
Module B2 includes an overview of global warming potential

## Slide 5: Common Emissions Impact Categories
Global Warming/Climate Change Potential (GWP)
Acidification Potential (AP)
Stratospheric Ozone Depletion Potential (ODP)
Smog/Ozone/Photochemical Oxidants/Creation Potential (SCP)
Human Health Particulates/Criteria Air Potential (HHCAP)
Human Health/Toxicity Cancer/Non-Cancer Potential (HTP)
Ecotoxicity Potential (ETP)
Eutrophication Potential (EP)
Air
Air
Water
Soil
Bolded impact categories are those covered in this module
These are only some of the possible impact categories in LCA

## Slide 6: Global Warming Potential (GWP)
Increase in greenhouse gas concentrations, resulting in potential increases in global average surface temperature
Often called climate change to reflect scope of possible effects
  Climate=long term Weather=short term
Occurs due to potential increased greenhouse effect from increased concentrations of greenhouse gases in the atmosphere
Some common greenhouse gases (GHGs) include:
  Carbon dioxide (CO2)
  Methane (CH4)
  Nitrous oxide (N2O)
  Ozone (O3)
  Water vapor (H2O) – Usually not considered anthropogenic
Figure source: USGCRP (2009). “Global Climate Change Impacts in the United States.”
Global
Scale of impacts:
CO2: carbon dioxide
Change in Average Global Surface Temperature
Based on one projection under various emissions scenarios

## Slide 7: Greenhouse Effect
Trapping of heat in by the troposphere by greenhouse gases due to differences in interaction with long wave and short wave radiation (acts like a blanket)
  Incoming radiation from the sun (long wave) is mostly allowed to pass through
  Outgoing re-radiated heat from the surface (short wave) is partially blocked
  Balance called radiative forcing
Some greenhouse effect needed to sustain natural temperatures
Additional effect from human activity is the concern
Figure source: livescience.com

## Slide 8: Possible Global Climate Change Effects??
Magnitudes of effects (endpoints) are more difficult to predict. These are just possible scenarios.
Figure source: epa.gov

## Slide 9: Some Observed Effects That Might Relate to GWP
Source: IPCC, 2014: Climate Change 2014: Synthesis Report. Geneva, Switzerland. <http://www.ipcc.ch/pdf/assessment-report/ar5/syr/SYR_AR5_FINAL_full.pdf>

## Slide 10: Characterization of Global Warming Potential
GWP= Σi (mi x GWPi)
where
GWP=global warming potential in kg CO2-eq of full inventory of GHGs
mi = mass (in kg) of inventory flow ‘i’,
GWPi = kg of carbon dioxide with the same heat trapping potential as one kg of inventory flow ‘i'
Note: Different groups and scientists have different lists of GWPi
1 kg of substance | GWPi (kg CO2-e)
Carbon dioxide (CO2) | 1
Methane (CH4) | 25
Nitrous oxide (N2O) | 298
Sulfur hexafluoride (SF6) | 22,800
Nitrogen trifluoride (NF3) | 17,200
Methyl bromide (CH3Br) | 5
Carbon tetrafluoride (CF4) | 7390
HCFC-134a (C2H2F4) | 1430
GWP100 (100-year basis) Characterization
Factors (from TRACI 2.1)

## Slide 11: Expanded GWP values
1 kg of substance | GWPi (100 year kg CO2-e) | MMT emitted in US in 2013 | MMT 100 yr CO2-eq in US in 2013 | Major Sources
Carbon dioxide (CO2) | 1 | 5,505 | 5,505 | Fossil fuel combustion
Methane (CH4) | 25 | 25 | 636.3 | Fermentation, natural gas, landfills, etc.
Nitrous oxide (N2O) | 298 | 1.2 | 355.2 | Agricultural soil management
Sulfur hexafluoride (SF6) | 22,800 | <0.0005 | 6.9 | Electrical distribution
Nitrogen trifluoride (NF3) | 17,200 | <0.0005 | 0.6 | Semiconductor manufacture
HFCs | 12-14,800 | Not available | 163 | ODP substance substitutes
PFCs | 7,390-12,200 | Not available | 5.8 | Aluminum production and semiconductor manufacture
Note: MMT is million metric tons (109 kg), ODP is ozone depletion potential, HFC and PFC ranges from http://www.epa.gov/climatechange/ghgemissions/gases/fgases.html
Values from Inventory of U.S. Greenhouse Gas Emissions and Sinks

## Slide 12: Major Sources and Sinks of Common GHGs
Sinks:
Oceans
  Photosynthesis (CO2)
  Dissolution (CO2)
  Sediment (CO2)
Sources:
  Fossil fuel combustion (CO2, CH4, N2O)
  Manufacture of cement (CO2)
  Land use change (CO2)
  Decomposition in landfills (CH4)
  Ruminant animal raising (CH4)
  Fertilizers (N2O)
Figure sources: epa.gov
Atmospheric
  Oxidation (CH4)
  Photolysis (N2O)
Land
  Limestone (CO2)
  Plant photosynthesis (CO2)
When sources increase and/or sinks decrease, concentrations may go up.

## Slide 13: Carbon Cycle
Image: www.esrl.noaa.gov/gmd/outreach/carbon_toolkit/images/carbon_cycle.jpg
Carbon is exchanged between sources and sinks
  Rates not known with absolute certainty
  Factors can affect sink rates, such as ocean currents for dissolution
  Higher CO2 concentrations could have effects on rates, such as uptake by plants

## Slide 14: Timescale for Global Warming
Different gases have different residence times in the atmosphere
  Only exert radiative forcing while present
  Losses due to sinks previously described
GWP is quantified based on increased radiative forcing over a period of time
  Usually 100 years is used
  Sometimes 20, 50, or 500 years may be used
Also, 1 ton of carbon dioxide released today and re-absorbed today is sometimes referred to as ‘carbon neutral’
  Much debate about what carbon neutrality means
Image Source: theoilconundrum.blogspot.com

## Slide 15: Residence Time of CO2
“For a given amount of carbon dioxide emitted, some fraction of the atmospheric increase in concentration is quickly absorbed by the oceans and terrestrial vegetation, some fraction of the atmospheric increase will only slowly decrease over a number of years, and a small portion of the increase will remain for many centuries or more.” (EPA 2015)
Source | Life (yr.)
Jacobson (2005) | 30-95
Heweitt and Jackson (2009) | 50-100
Stumm and Morgan (1996) | 7
Archer and Brovkin (2008) | Hundreds of thousands
Hewitt, C. N., and Andrea V. Jackson. Atmospheric Science for Environmental Scientists. Chichester, U.K.: Wiley-Blackwell, 2009. Print.
Archer, D. and Brovkin, V. (2008). “The millennial atmospheric lifetime of anthropogenic CO2.” Climate Change, 90:283-297.
Jacobson, MZ (2005). "Correction to "Control of fossil-fuel particulate black carbon and organic matter, possibly the most effective method of slowing global warming."". J. Geophys. Res. 110. pp. D14105.
Figure source: Archer, D. and Brovkin, V. (2008). “The millennial atmospheric lifetime of anthropogenic CO2.” Climate Change, 90:283-297.

## Slide 16: Characterization of GWP at Different Timescales
1 kg of substance | Life (yr.) | GWP20 | GWP100 | GWP500
Carbon dioxide | Variable | 1 | 1 | 1
Methane | 12 | 72 | 25 | 8
HCFC-134a (C2H2F4) | 14 | 3,830 | 1,430 | 435
Nitrous oxide | 120 | 289 | 298 | 153
Nitrogen trifluoride | 740 | 12,300 | 17,200 | 20,700
Sulfur hexafluoride | 3200 | 16,300 | 22,800 | 32,600
Carbon tetrafluoride | 50,000 | 5,210 | 7,390 | 11,200
Note: Lifetimes from Klopffer and Grahl (2014). GWP values from CML 2007
Different GWPs cannot be compared to one another

## Slide 17: Biogenic CO2
Biogenic CO2 is that released from recently living materials, such as:
Often assumed to have net zero release of CO2
  Assumption that CO2 released is recaptured during re-growth
  Many factors may make this a poor assumption in some cases
    Time lag between emissions and regrowth
    Changes in soil organic matter
    Changes in land use
    Many more
Therefore, there is much discussion on best practices to attempt to quantify these effects, rather than simply assuming carbon neutrality which may not be applicable in all cases.
Wood: mtlfd.org Ethanol: eworld.com Wastewater: mottmac.com Carbon neutral: wheildons.co.uk
?
Wood
Ethanol
Wastewater Treatment

## Slide 18: Global Warming Potential Example Calculation
Example Problem:
Average conventional diesel fuel production, including extraction of crude oil, transportation, and refining produces the following greenhouse gas emissions per gallon of fuel produced:
  14.9 g of CH4
  31.0 mg of N2O
  2.35 kg of CO2
  Using only these emissions data, calculate the global warming potential of conventional diesel production expressed in kg CO2-equivalent using a 100-year time frame.
Data sourced from GREET for U.S. National Average Refineries

## Slide 19: Global Warming Potential Example Calculation
GHG emissions inventory=14.9 g of CH4, 31.0 mg of N2O, 2.35 kg of CO2
  Calculate the global warming potential in kg CO2-equivalent (kg CO2e).
Look up 100-year characterization factors for CH4, N2O, and CO2
  Methane (CH4): 25 kg CO2-eq per kg CH4
  Nitrous Oxide (N2O): 298 kg CO2-eq per kg of N2O
  Carbon Dioxide (CO2): 1 kg CO2-eq per kg of CO2
Convert emissions to kg CO2-eq
Sum all emissions in kg CO2-eq to find global warming potential:

## Slide 20: Global Warming Potential Example Calculation
Example Problem:
All processes involved in the production of corn (to be used for ethanol) result in the following greenhouse gas emissions per US bushel of corn produced:
  8.3 g of CH4
  15.0 g of N2O
  3.94 kg of CO2
  Using only these emissions data, calculate the global warming potential of corn production expressed in kg CO2-equivalent using a 20-year time frame.
Data sourced from GREET

## Slide 21: Global Warming Potential Example Calculation
GHG emissions inventory=8.3 g of CH4, 15.0 g of N2O, 3.94 kg of CO2
  Calculate the global warming potential in kg CO2-equivalent (kg CO2e).
Look up 20-year characterization factors for CH4, N2O, and CO2
  Methane (CH4): 72 kg CO2-eq per kg CH4
  Nitrous Oxide (N2O): 289 kg CO2-eq per kg of N2O
  Carbon Dioxide (CO2): 1 kg CO2-eq per kg of CO2
Convert emissions to kg CO2-eq
Sum all emissions in kg CO2-eq to find global warming potential:

## Slide 22: GWP20, GWP100, and GWP500 Comparison
Contribution From | GWP20 | GWP100 | GWP500
CO2 (kg CO2-eq) | 2.35 | 2.35 | 2.35
CH4 (kg CO2-eq) | 1.07 | 0.37 | 0.11
N2O (kg CO2-eq) | 0.01 | 0.01 | 0.005
Total (kg CO2-eq) | 3.43 | 2.73 | 2.47
Contribution From | GWP20 | GWP100 | GWP500
CO2 (kg CO2-eq) | 3.94 | 3.94 | 3.94
CH4 (kg CO2-eq) | 0.60 | 0.21 | 0.06
N2O (kg CO2-eq) | 4.34 | 4.47 | 2.30
Total (kg CO2-eq) | 8.88 | 8.62 | 6.30
Production of 1 gallon of diesel fuel
Production of 1 US bushel of corn
GWPs between different time frames cannot be directly related to one another

## Slide 23: What time frame should we use?
Likely depends on the goal and intended use of the LCA
For example:
a) If goal is reduce global warming by 2035, maybe 20 year GWP might be most appropriate
b) If the goal is to decrease GWP by 2115, maybe 100 year GWP might most appropriate (but may be hotter in 2035 than in scenario a)
This question is difficult to answer, but at least should be considered anytime an LCA is carried out or interpreted
Clock: clker.com
?

## Slide 24: Global Warming Potential (GWP) Summary
*Ryberg et al. 2014 Glacier: nrmsc.usgs.gov
Increase in severe weather frequency
Sea level increase
CO2
Main substances*
Increased radiative forcing (trapping heat)
Midpoint
Fuel combustion
Electricity
Major sources
Agriculture
80%
CH4
9%
N2O, O3, H2O(g), CFCs, Others
Increase in heat-related illnesses
Some Possible Endpoints
Transportation
Industrial processes
11%
Wind and ocean current changes
Soil moisture loss
CO2: carbon dioxide CH4: methane N2O: nitrous oxide O3: ozone H2O(g): water vapor CFC: chlorofluorocarbons
Percentages of impact contributed by each substance is based on total US inventory from Ryberg et al. 2014 and represents the percentage of impacts, not mass

## Slide 25: Thank you for completing Module β1!
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules

## Slide 26: Homework
Find 2 carbon footprint studies and explain what timescales they use and why
Convert those results to 20 and 500 year timescales