## Slide 1: Welcome to the Life Cycle Assessment (LCA) Learning Module Series
Acknowledgements:
CESTiCC Washington State University Fulbright
Liv Haselbach Quinn Langfitt
For current modules email haselbach@wsu.edu or visit cem.uaf.edu/CESTiCC

## Slide 2: LCA Module Series Groups
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules

## Slide 3: Acidification Potential
Module β2
It is suggested to review Modules B1 and B2 prior to this module

## Slide 4: Summary of Module B1 and Other Points
All impacts are “potential”
Only anthropogenic sources are included
Different substances have different relative amounts of forcing
  Usually results are related to the equivalent release of a particular substance
Different impact categories have different scales of impacts
  Global, regional, local
Watch Module B1 for background
Module B2 includes a brief overview of acidification potential

## Slide 5: Common Impact Categories
Global Warming/Climate Change Potential (GWP)
Acidification Potential (AP)
Stratospheric Ozone Depletion Potential (ODP)
Smog/Ozone/Photochemical Oxidants/Creation Potential (SCP)
Human Health Particulates/Criteria Air Potential (HHCAP)
Human Health/Toxicity Cancer/Non-Cancer Potential (HTP)
Ecotoxicity Potential (ETP)
Eutrophication Potential (EP)
Mainly
Air
Air
Water
Soil
Bolded impact categories are those covered in this module
These are only some of the possible impact categories in LCA

## Slide 6: Acidification Potential (AP)
Emissions which increase acidity (lower pH) of water and soils
Major substances:
  Sulfur oxides (SOx)
  Nitrogen oxides (NOx)
  Ammonia (NH3)
These can travel some distance before being deposited
Deposition routes include
  Wet (Acid rain) (most common form)
  Dry
  Cloud
Image source: blog.epa.gov
Local
Regional
Scale of impacts:

## Slide 7: Acidification Potential
Changes in hydrogen ion concentration (i.e. pH)
  Some organisms are sensitive (only thrive in limited pH range)
  Even those not sensitive can be harmed through food chain
Usually midpoint characterized as:
  mol H+-eq
  kg SO2-eq (1 kg SO2-eq ≈ 50.8 mol H+-eq)
Endpoint effects include:
  Death of animals (like fish)
  Death of plants (especially forests)
  Damage to manmade materials (such as buildings)
pH scale: edu.pe.ca Species sensitivity: epa.gov

## Slide 8: Characterization of Acidification Potential
AP= Σi (mi x APi)
where
AP=acidification potential of full inventory in kg SO2-eq
mi = mass (in kg) of inventory flow i,
APi = kg of sulfur dioxide with the same acidification potential as one kg of inventory flow ‘i'
Note: characterization factors for AP are usually based on stoichiometry of moles H+ released
1 kg of substance | APi (kg SO2-e)
Ammonia (NH3) | 1.88
Hydrogen Chloride (HCl) | 0.88
Hydrogen Fluoride (HF) | 1.60
Hydrogen Sulfide (H2S) | 1.88
Nitrogen Oxides (NOx as NO2) | 0.70
Sulfur Oxides (SOx as SO2) | 1
Sulfuric Acid (H2SO4) | 0.65
AP Characterization Factors (TRACI 2.1)

## Slide 9: What is SOx?
SOx = Sulfur Oxides
Includes:
  Lower sulfur oxides (SnO, S7O2 and S6O2)
  Sulfur monoxide (SO)
  Sulfur dioxide (SO2)
  Sulfur trioxide (SO3)
  Higher sulfur oxides (SO3+x where 0<x≤1)
  Particulate sulfates (SO4s)
Sulfur dioxide (SO2) is predominant form found in the lower atmosphere and forms sulfurous acid (H2SO3) when dissolved in atmospheric water
Major anthropogenic sources:
  Combustion of fossil fuels in:
    Power plants
    Industrial facilities
    High sulfur fuels in mobile sources
  Industrial processes (e.g. extracting metal from ores)
Container ship: maritime-connector.com Power plant: energywisepa.org Truck: huffingtonpost.com

## Slide 10: What is NOx?
NOx = Nitrogen Oxides
Includes:
  Nitrogen monoxide (NO)
  Nitrogen dioxide (NO2)
  Nitrous oxide (N2O) – Sometimes omitted
NO2 emitted directly
  NO also converts to NO2 in the atmosphere
When NO2 dissolves in atmospheric water it is converted to nitric acid (HNO3)
Major source is combustion of fuels
  Air is mostly nitrogen
  Most passes through combustion unchanged (i.e. N2 in, N2 out)
  Some combines with oxygen at high temperature to form NOx
Combustion from:
  Stationary power generation
  Cars, trucks, and buses
  Off-road vehicles/equipment
Power plant: earthmagazine.org Road: nytimes.com Off road: media.noria.com

## Slide 11: Regional variation
Regional variations can be quite important
  Different local plant and animal species
  Different levels of current pH balance (proximity to critical loads)
  Different buffering capacities
  Different pollutant transport properties
Some effort has gone into quantifying these differences
  Regional characterization factors and non-linear assessment methods
  State-by-state characterization factors available in TRACI
  State factors vary from 20% to 160% of overall US average
Figure source: eea.europa.eu

## Slide 12: Acidification of Oceans
Acidification of oceans hard to quantify
  Ocean have high buffering capacity
  Note: this impact category does not include acidification by CO2 dissolution into oceans
Figure Source: usa.oceana.org

## Slide 13: Acidification Potential (AP)
*Ryberg et al. 2014 Building damage: h2owash.biz Forest: Britannica.com Power plant: ehow.com
Plants (esp. forests)
Organisms
NOx
Main substances*
Increased soil and water acidity
Midpoint
Fuel combustion
Electricity
Major sources
Agriculture
38%
SOx
35%
NH3
26%
Others: 1%
Buildings
Possible Endpoints
Transportation
NOx: nitrogen oxides SOx: sulfur oxides NH3: ammonia

## Slide 14: Thank you for completing Module β2!
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules

## Slide 15: Homework
Identify three aquatic species that live in your area and briefly research their sensitivity to acidity increase. What might happen if those species were to die as a result of acid rain?
Think about the industries, sources of electricity, density of vehicle use, etc. in your home region and estimate which sources of acidification (NOx, SOx, NH3) might be most prevalent. Why do you think that?