## Slide 1: Welcome to the Life Cycle Assessment (LCA) Learning Module Series
Acknowledgements:
CESTiCC Washington State University Fulbright
Liv Haselbach Quinn Langfitt
For current modules email haselbach@wsu.edu or visit cem.uaf.edu/CESTiCC

## Slide 2: LCA Module Series Groups
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules

## Slide 3: Ozone Depletion Potential
Module β3
It is suggested to review Modules B1 and B2 prior to this module

## Slide 4: Summary of Module B1 and Other Points
All impacts are “potential”
Only anthropogenic sources are included
Different substances have different relative amounts of forcing
  Usually results are related to the equivalent release of a particular substance
Different impact categories have different scales of impacts
  Global, regional, local
Watch Module B1 for background
Module B2 includes a brief overview of ozone depletion potential

## Slide 5: Common Impact Categories
Acidification Potential (AP)
Global Warming/Climate Change Potential (GWP)
Stratospheric Ozone Depletion Potential (ODP)
Smog/Ozone/Photochemical Oxidants/Creation Potential (SCP)
Human Health Particulates/Criteria Air Potential (HHCAP)
Human Health/Toxicity Cancer/Non-Cancer Potential (HTP)
Ecotoxicity Potential (ETP)
Eutrophication Potential (EP)
Air
Air
Water
Soil
Bolded impact categories are those covered in this module
These are only some of the possible impact categories in LCA

## Slide 6: Ozone
Ozone molecule: naturallythebest.com Good/bad ozone: epa.gov
Molecule composed of three oxygen atoms
Colorless, odorless gas
The focus of two very different impact categories
  Ozone depletion potential – “Good” ozone
  Smog creation potential – “Bad” ozone

## Slide 7: Ozone Profile
“Good” Ozone
“Bad” Ozone
Image source: NOAA. (2006). “The Science of Ozone Depletion” <www.esrl.noaa.gov/csd/assessments/ozone/2006/twentyquestionsposter.pdf>

## Slide 8: Ozone Depletion Potential (ODP)
Reduction of ozone concentration in the stratosphere
This is “good” ozone which filters out UV-B radiation
Additional UV can cause negative effects on humans, crops, and the built environment
Occurs when ozone depleting substances catalyze ozone destroying reactions
First noticed by scientists in 1970s
Two phenomena covered by this impact category
  Decreased overall ozone concentration in the stratosphere
  More severe depletion in localized holes (e.g. the ozone hole)
Not a major cause of global warming/climate change
Some time dependence, but usually not accounted for in LCA
Global
Scale of impacts:

## Slide 9: Process and Effects of Ozone Depletion
Emissions of ozone depleting substances
Substances are transported to stratosphere where Cl- and Br- detach
Ozone depleted based on substance’s reactivity/lifetime
Reduced ozone allows increased UVB penetration
Effects of increased UV:
Skin cancer
Cataracts
Damage to:
Crops
Materials
Marine life
Midpoint
Endpoint
Flow diagram adapted from: Bare, J., Norris, G., Pennington, D., and McKone, T. (2002). “Traci.” Journal of Industrial Ecology, 6(3‐4), 49-78.
Image source: epa.gov

## Slide 10: Substances
Due to decreases in emissions of these, N2O (laughing gas) is becoming important
  Will likely be largest contributor to ODP in 21st century according to Ravishankara et al. (2009)
  Causes ozone loss through different mechanism
  Main anthropogenic emissions from agriculture and fuel combustion
  Not even classified as ODP in most impact methodologies (including TRACI 2.1 and CML 2007)
Abbrev. | Name | Severity | Main use(s) | Some Examples*
Halons | Haloalkanes | Very high | Fire suppression | Halon 1301, Halon 1211
CFCs | Chlorofluorocarbons (Freons) | High | Refrigeration, A/C, aerosols, solvents | CFC-11, CFC-12
HCFCs | Hydrochlorofluorocarbons | Moderate | Refrigeration, A/C, aerosols, solvents | HCFC-140, HCFC-22
*Common naming (e.g. CFC-11) is based on numbering scheme for # of C atoms, # of H atoms, # of F atoms, and # of Br atoms
Classes of Ozone Depleting Substances (Selection)

## Slide 11: Stratospheric Ozone Chemistry
O2 + hν
2O
2O
2O3
Formation
Destruction
Sun
Step 1
+
2O2
Step 2
O3 + hν
O
Sun
Step 1
O2
+
O3
O
Step 2
2O2
+
Happens at equal rates in natural equilibrium

## Slide 12: Chlorine/Bromine Catalyzed Reaction
Chlorine and bromine travel to the stratosphere attached to CFCs, HCFCs, Halons, etc.
After some time, the chlorine or bromine atoms break off in reaction with sunlight in the stratosphere
They can then catalyze ozone destruction through the following sequence
O2
+
+
O3
O2
ClO
Cl
ClO
+
Cl
+
Step 1
Step 2
O

## Slide 13: Characterization of Ozone Depletion Potential
ODP= Σi (mi x ODPi)
where
ODP=ozone depletion potential of full inventory in kg CFC-11-eq
mi = mass (in kg) of inventory flow i,
ODPi = kg of CFC-11 with the same ozone depletion potential as one kg of inventory flow ‘i‘
  Based on each substance’s reactivity and lifetime
1 kg of substance | ODPi (kg CFC-11-eq)
Carbon Tetrachloride (CCl4) | 0.73
CFC-12 (CCl2F2) | 1.00
Halon 1301 (CF3Br) | 16.0
HCFC-22 (CHF2Cl) | 0.05
Methyl Bromide (CH3Br) | 0.51
Trichloroethane (1,1,1-CH3CCl3) | 0.12
Nitrous Oxide (N2O)* | 0.017
ODP Characterization Factors (TRACI 2.1)
  *Not characterized in TRACI 2.1, value from Ravishankara et al. (2009)

## Slide 14: Ozone Hole
Extensive localized losses
  Mostly at arctic and Antarctic
Antarctic hole most severe
  Largest in springtime
Polar holes due to presence of polar stratospheric clouds (PSCs - ice clouds) and due to relative isolation of air transport there in the winter
  Convert HCl and ClONO2 into ClO (more reactive)
  Enhanced destruction of ozone
  Minimum temperature and sustained low temperature for PSC formation more common in Antarctic
Hole: Wikipedia.org PSC and Formation Conditions: NOAA. (2006). “Twenty Questions: 2006 Update.”
Polar Stratospheric Clouds

## Slide 15: Montreal Protocol
International treaty to limit the production and use of ozone depleting substances
Agreed upon in 1987, and enforced starting in 1989
Universally ratified by the United Nations members
Phase out of harmful substances, phase in of less harmful replacements
  First phase out CFCs (high ODP)
  Then phase out HCFCs (moderate ODP)
  Various others: halons, carbon tet, etc.
  Replace mostly by HFCs (no ODP)
Significant reduction in ODP emissions
Recovery of ozone hole expected within about 50 years (EPA 2010)
EPA. (2010). “Ozone Science: The Facts Behind the Phaseout” <http://www.epa.gov/ozone/science/sc_fact.html>).
Fig: Fahey and Hegglin. (2010). “20 Q’s and A’s About the Ozone Layer.”

## Slide 16: Ozone Depletion Potential (ODP)
Skin cancer
Halon 1301
Main substances*
Decrease in stratospheric ozone concentration
Midpoint
Manufacturing (polymers, aerosols)
Major sources
Refrigerant systems
29%
CFC-11
22%
Others: 26%
Possible Endpoints (Due to increased UV-B radiation)
Fire extinguishers
Crop damage
*Ryberg et al. 2014
Materials damage
Marine life damage
CFC-12
14%
HCFC-22
9%
CFC: chlorofluorocarbon HCFC: hydrochlorofluorocarbon
www.esrl.noaa.gov/csd/assessments/ozone/2006/twentyquestionsposter.pdf

## Slide 17: Thank you for completing Module β3!
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules

## Slide 18: Homework
Look around your home, school, or office building and identify potential sources of gases that might contribute to ozone depletion.
Follow the link on Slide 16 to the full size poster. From those topics covered on the poster, choose one not covered in this module that interests you and explain what the poster says about it in your own words.
Research what your country or state has done to reduce ozone depletion. Briefly summarize (a few sentences) one piece of legislation or one program that has been enacted to reduce ozone depletion.