## Slide 1: Welcome to the Life Cycle Assessment (LCA) Learning Module Series
Acknowledgements:
CESTiCC Washington State University Fulbright
Liv Haselbach Quinn Langfitt
For current modules email haselbach@wsu.edu or visit cem.uaf.edu/CESTiCC

## Slide 2: LCA Module Series Groups
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules

## Slide 3: Smog Creation Potential
Module β4
It is suggested to review Modules B1 and B2 prior to this module

## Slide 4: Summary of Module B1 and Other Points
All impacts are “potential”
Only anthropogenic sources are included
Different substances have different relative amounts of forcing
  Usually results are related to the equivalent release of a particular substance
Different impact categories have different scales of impacts
  Global, regional, local
Watch Module B1 for background
Module B2 includes a brief overview of smog creation potential

## Slide 5: Common Impact Categories
Global Warming/Climate Change Potential (GWP)
Acidification Potential (AP)
Stratospheric Ozone Depletion Potential (ODP)
Smog/Ozone/Photochemical Oxidants/Creation Potential (SCP)
Human Health Particulates/Criteria Air Potential (HHCAP)
Human Health/Toxicity Cancer/Non-Cancer Potential (HTP)
Ecotoxicity Potential (ETP)
Eutrophication Potential (EP)
Mostly
Air
Air
Water
Soil
Bolded impact categories are those covered in this module
These are only some of the possible impact categories in LCA

## Slide 6: Ozone
Ozone molecule: naturallythebest.com Good/bad ozone: epa.gov
Molecule composed of three oxygen atoms
Colorless, odorless gas
The focus of two very different impact categories
  Ozone depletion potential – “Good” ozone
  Smog creation potential – “Bad” ozone

## Slide 7: Ozone Profile
“Good” Ozone
“Bad” Ozone
Image source: NOAA. (2006). “The Science of Ozone Depletion” <www.esrl.noaa.gov/csd/assessments/ozone/2006/twentyquestionsposter.pdf>

## Slide 8: Smog Creation Potential (SCP)
Increased formation of ground-level ozone
  Also called photoxidant formation, ozone creation, etc.
  Formed from reactions of NOx, VOCs, other pollutants, and sunlight
  Can have effects on human health and vegetation
Effects vary, but LCA does not usually capture, based on:
  Current air composition (i.e. NOx or VOC limited)
  Time of day and year (sunlight)
  Physical characteristics of area and weather patterns
  Exposed populations
Commonly expressed as:
  kg O3-equivalent
  kg C2H4-equivalent
  kg NOx-equivalent
Image source: edmunds.com
Scale of impacts:
Local
O3: ozone C2H4: ethane NOx: nitrogen oxides VOCs: volatile organic compounds

## Slide 9: What is Smog?
Term coined from combining the words smoke and fog
  Originally used to refer to pollution in London in the 19th century from coal emissions
Modern smog (being addressed in this impact category) is different
  Sometimes called photochemical smog
  Main compound is ground-level ozone
  Other constituents include:
    Peroxyacetyl nitrates
    Aldehydes,
    Remaining NOx and VOCs (not converted to ozone)
Image source: culturacolectiva.com

## Slide 10: Effects of Smog
Human health
  Eye irritation
  Respiratory tract irritation
  Lung irritation
  Reduced lung function
  Aggravation of asthma
Vegetation
  Crops
  Forests
Quality of Life
  Decreased visibility (such as for seeing landmarks)
Mostly short term effects
Some worry chronic short term
effects could lead to long term ones
Some populations at higher risk
  Children
  Elderly
  Those with pre-existing respiratory conditions
  Those who work outside

## Slide 11: Requirements for Smog Formation
Requirements for forming ground level ozone:
  Solar radiation
  Reactive nitrogen oxides (NOx)
  Reactive volatile organic compounds (VOCs) and/or carbon monoxide (CO)
Major anthropogenic source is vehicle emissions
Major natural source is forests
Car exhaust: rjdaviesmotor.com Forest: fs.usda.gov Sun: radnorlibrary.org
VOCs
Organic chemicals with a low boiling point (<250°C at 1 atm pressure).
Hundreds of chemicals fall under this distinction.

## Slide 12: Smog Creation Chemistry – NOx Cycle
NO2 + hν
NO
O
O3
Sun
1)
+
O2
2)
+
O
O3
3)
NO
+
NO2
O2
+

## Slide 13: Smog Creation Chemistry – NOx and HOX
NO2 + hν
NO
O
O3
NOx Cycle
Sun
1)
+
O2
2)
+
O
CO
NO
HOx Cycle (example with CO)
1)
+
HO2
3)
+
HO
+
CO2
NO2
+
HO
O3
3)
NO
+
NO2
O2
H
H
2)
+
HO2
O2
+
Creates NO2 from NO without destroying ozone

## Slide 14: Characterization of Smog Creation Potential
SCP= Σi (mi x SCPi)
where
SCP=smog creation potential of full inventory in kg O3-eq
mi = mass (in kg) of inventory flow i,
SCPi = kg of O3 that would be released (though O3 is rarely emitted directly) for the same smog creation as one kg of inventory flow ‘i'
1 kg of substance | SCPi (kg O3-eq)
Nitric oxide | 24.8
Nitrogen dioxide | 16.8
VOCs (in general) | 3.6
Butene (1-Butene) | 9.7
Formaldehyde | 9.5
Carbon monoxide | 0.056
Acetaldehyde | 6.5
Methane | 0.014
SCP Characterization Factors (TRACI 2.1)
Methane should not be aggregated with other VOCs for
SCP characterization, it has a much lower SCPi than most

## Slide 15: Importance of Regional Variation – Topography and Climate
Landscape features like canyons can trap pollutants
  Limits air circulation
  Can cause air inversions
Similar phenomenon can happen in a “street canyon” between buildings in urban environment
Solar insolation drives reactions so they are more likely to occur where there is significant sun (temporal resolution important here too)
A few examples of these conditions:
  Los Angeles, CA, USA
  Denver, CO, USA
  Mexico City, Mexico
  Santiago, Chile
Los Angeles: pulsoverde.nrdc.org Mexico City: cdn.zmescience.com
Los Angeles
Mexico City

## Slide 16: Importance of Regional Variation – Preexisting Air Composition
Preexisting NOx and VOC concentrations are important
In VOC limited area, NOx emission will have little impact (and vice versa)
Most VOCs concentration from forests in many regions
  About 90% is typical in rural USA
  About 10-40% is typical in urban USA
  Cannot control these, so often NOx control is the main focus
Image source: oceanworld.tamu.edu

## Slide 17: Some Efforts to Account for Regional Variation
TRACI incorporates:
  Relative influence of NO­­x vs VOC
  Impact by state (location specific)
  “Methods for aggregation of effects among receiving states by area” (Bare et al. 2002)
RAINS (Developed by UNECE)
  Regional Air Pollution Information and Simulation
  Impact by country in Europe
  Relates emissions of precursors to O3 concentration at receptor site
Shah and Ries (2009)
  Spatial and temporal resolution for 48 US states and Washington DC
  Based on combination of MM5-SMOKE-CAMx for meteorology, emissions, and chemistry and transport, respectively
Shah, V.P, and Ries R.J. (2009). “A characterization model with spatial and temporal resolution…United States.” Int. J Life Cycle Assess, 14, 313-327.

## Slide 18: Smog Creation Potential (SCP)
Reduced lung function/aggravation
NOx
Main substances*
Increase in ground-level
ozone concentration
Midpoint
Cars and other vehicles
Major sources
Energy production
87%
VOCs
11%
Others: 2%
Possible Endpoints
Industrial processes
Aggravate Asthma
*Ryberg et al. 2014 Image source: science.nature.nps.gov
Vegetation damage
Eye irritation
NOx: nitrogen oxides VOCs: volatile organic compounds
2005-2009 4th highest annual value of maximum daily 8-hr. ozone in ppb

## Slide 19: Thank you for completing Module β4!
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules

## Slide 20: Homework
Estimate how much of an issue you would expect smog to be in your current city versus one other city of your choosing, based on sources, topography, sunlight, etc.
Look up the actual average ozone concentration (or whatever you can find. e.g. 4th highest annual maximum) of the two cities. If it differs from your expectation, think of what other factors might be at play and discuss them.
Which of the effects of smog from Slide 10 would likely be an issue in your current city, assuming that smog were present.