## Slide 1: Welcome to the Life Cycle Assessment (LCA) Learning Module Series
Acknowledgements:
CESTiCC Washington State University Fulbright
Liv Haselbach Quinn Langfitt
For current modules email haselbach@wsu.edu or visit cem.uaf.edu/CESTiCC

## Slide 2: LCA Module Series Groups
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules

## Slide 3: Eutrophication Potential
Module β5
It is suggested to review Modules B1 and B3 prior to this module

## Slide 4: Summary of Module B1 and Other Points
All impacts are “potential”
Only anthropogenic sources are included
Different substances have different relative amounts of forcing
  Usually results are related to the equivalent release of a particular substance
Different impact categories have different scales of impacts
  Global, regional, local
Watch Module B1 for background
Module B3 includes a brief overview of eutrophication potential

## Slide 5: Common Impact Categories
Acidification Potential (AP)
Global Warming/Climate Change Potential (GWP)
Stratospheric Ozone Depletion Potential (ODP)
Smog/Ozone/Photochemical Oxidants/Creation Potential (SCP)
Human Health Particulates/Criteria Air Potential (HHCAP)
Human Health/Toxicity Cancer/Non-Cancer Potential (HTP)
Ecotoxicity Potential (ETP)
Eutrophication Potential (EP)
Air
Air
Water
Soil
Bolded impact categories are those covered in this module
These are only some of the possible impact categories in LCA

## Slide 6: Eutrophication Potential
Excessive biological activity of organisms due to over-nutrification
  Also called nutrification
  Especially in aquatic systems, often apparent through algal blooms
  Can lead to oxygen deficiency in water killing aquatic life
Mostly forced by nitrogen and phosphorus
Organisms need nutrients to grow, but too much can have undesirable consequences
Local variations can be very important
In addition to water, also soil impacts
Source: ecodetail.net.au
Scale of impacts:
Local
Regional

## Slide 7: Main Substances and Sources
Eutrophying substances are nutrients, and when in excess, may be pollutants
Nitrogen and phosphorus are the main nutrients of interest
  Various forms and pathways of release for each
Sources of these nutrients include:
  Agriculture: Animal manure and excess fertilizer
  Storm water: Collects nutrients and pollutants from roads, roofs, etc.
  Wastewater: Sometimes nitrogen or phosphorus removal can be low these can be discharged in the effluent
  Fossil fuels: For electricity, transport, industry, etc. (emits nitrogenous compounds to the air)
  Home activities: Fertilizers, pet waste, detergents, and soaps
Cars in traffic: apr.org All other images: EPA. “Sources and Solutions.” Nutrient Pollution. epa.gov

## Slide 8: Characterization of Eutrophication Potential
EP= Σi (mi x EPi)
where
EP=eutrophication potential in kg N-eq (alternate units also used such as kg P-eq)
mi = mass (in kg) of inventory flow i,
EPi = kg of nitrogen with the same eutrophication potential as one kg of inventory flow ‘i‘
1 kg of substance | EPi (kg N-eq)
Ammonia (to water) | 0.78
Ammonia (to air) | 0.12
Nitrogen Oxides (as NO2 to air) | 0.04
Nitrate (to water) | 0.237
BOD | 0.05
COD | 0.05
Phosphorus to air | 1.12
Phosphorus to water | 7.29
EP Characterization Factors (TRACI 2.1)

## Slide 9: BOD and COD as Eutrophying “Substances”
Oxygen demand is not a particular substance or a nutrient
  It’s a surrogate for measuring organic matter present in the water
Oxygen demand (BOD or COD) is sometimes considered as having a eutrophication potential since it directly contributes to the endpoint effects of depleting oxygen from a lake
  Same effects that algae has when it is broken down after it dies
Only one or the other should be characterized
  If characterizing both, double counting is occuring
Biochemical Oxygen Demand
“Amount of oxygen consumed by microorganisms in decomposing organic matter in water”*
*http://water.epa.gov/type/rsl/monitoring/vms52.cfm **Standard Methods for the Examination of Water and Wastewater, 19th Edition.
BOD
Chemical Oxygen Demand
“A measure of the oxygen equivalent of the organic matter content of a sample that is susceptible to oxidation by a strong chemical oxidant.”**
COD
Easier to measure
Better metric for these processes

## Slide 10: Limiting Nutrient Concept
Nutrients such as nitrogen and phosphorus are used for biological growth in fairly uniform ratios
Sometimes one nutrient will be shorter supply than the other(s) and once exhausted, new cells will not be able to grow. Adding more of the other nutrient(s) will have little or no effect, while adding the limiting nutrient can have a large effect.
Nitrogen Limited
nitrogen
biomass
If we
then
phosphorus
biomass
If we
then
Phosphorus Limited
nitrogen
biomass
If we
then
phosphorus
biomass
If we
then

## Slide 11: Typical Limiting Nutrients By Setting
Nitrogen Limited
Fresh Water
Typically Phosphorus Limited
Ocean: funmozar.com
Soil: betterground.org
River algal bloom: eutro.org
Ocean eutrophication: earthuntouched.com/
Algal bloom lake: azores-adventures.com
Soil and Salt Water
Typically Nitrogen Limited
  Midpoints
  kg NO3—equivalent (nitrate)
  kg N-equivalent (nitrogen)
  Midpoints
  kg PO43- -equivalent (phosphate)
  kg P-equivalent (phosphorus)

## Slide 12: Deposition and Transport
Can be deposited by:
  Directly running off into water or soil
  Being emitted to air and subsequently deposited to water or soil
Just because a substance is emitted, doesn’t mean it gets to the water or soil
  For example, may be absorbed by plants along the way
  Or for fertilizers, most of the applied fertilizer is absorbed by crops as intended. Only some becomes runoff depending on slope, precipitation, volatilization, and biological availability
Alternatively, nutrients can travel a long way
  Phosphorus emitted in a region where it is not the limiting nutrient could be transported to a region where it is
  Why eutrophication can have regional scale of impacts
Characterization factors may have transport and fate built into them, particularly if regionalized

## Slide 13: Effects of Eutrophication
*www2.epa.gov/nutrientpollution/effects
Biodiversity: cbd.int fish kill: toxics.usgs.gov shellfish: nem.org.uk tourist: bphw.wikispaces.com swimming: doheny.com tap water: bu.edu

## Slide 14: Regional Variation
More of an issue if near or above the “critical load”
If well below the critical load, adding some nutrients is less likely to cause overgrowth of organisms
As can be seen, regions of high population are more likely to exceed the critical load
Some impact methodologies have separate regional characterization factors
  One example is TRACI
  Regions consisting of 9 groups of states
Sometimes regulated through total maximum daily loads (TMDL)
In mol N-eq/hectare-yr
Figure source: European Environment Agency. (2013). “Exposure of ecosystems to acidification, eutrophication, and ozone.”

## Slide 15: Eutrophication Potential
Loss of biodiversity
Death of aquatic life
Nitrogen
Main substances*
Excessive biological growth, especially of algae
Midpoint
Fossil fuel Combustion
Major sources
Storm and wastewater
42%
Phosphorus
33%
NH3
7%
Others: 8%
Foul odor
Possible Endpoints (mostly due to aquatic oxygen depletion)
Agricultural runoff
Septic field seepage
Water
NOx
10%
Air
esp. freshwater
esp. marine
Toxicity to humans
*Ryberg et al. 2014

## Slide 16: Thank you for completing Module β5!
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules

## Slide 17: Homework
What is the nearest body of water to your house or university? Using assumptions presented in this module on typical limiting nutrients, would a large release of phosphorus be expected to result in an increase in biomass concentration in that water body?
Look up the discharge characteristics of a local wastewater treatment plant. If you cannot find one in your area follow the link at the bottom of the slide for the Pullman, WA treatment plant. Using the average values of daily discharge and the characterization factors on slide 8, calculate the annual eutrophication potential of the discharge (only for those substances with factors on slide 8, although that is simply a sampling of characterized substances).
https://fortress.wa.gov/ecy/wqreports/public/WQPERMITS.document_pkg.download_document?p_document_id=119464