## Slide 1: Welcome to the Life Cycle Assessment (LCA) Learning Module Series
Acknowledgements:
CESTiCC Washington State University Fulbright
Liv Haselbach Quinn Langfitt
For current modules email haselbach@wsu.edu or visit cem.uaf.edu/CESTiCC

## Slide 2: LCA Module Series Groups
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules

## Slide 3: Human Health Particulate Matter
Module β7
It is suggested to review Modules B1 and B3 prior to this module

## Slide 4: Summary of Module B1 and Other Points
All impacts are “potential”
Only anthropogenic sources are included
Different substances have different relative amounts of forcing
  Usually results are related to the equivalent release of a particular substance
Different impact categories have different scales of impacts
  Global, regional, local
Watch Module B1 for background
Module B3 includes a brief overview of human health particulates potential

## Slide 5: Human Health – Particulates
Health issues related to increased respiration of very small particles
  Small particles released directly and formed through secondary reactions
  Both solids and liquid droplets
  When breathed into lungs may cause respiratory disease and cancer
Category also called “criteria air pollutants”, but really only deals with subset
This category doesn’t deal with toxicity related to the specific substances
  Only based on the size of the particles, not their composition
  Therefore, less uncertainty about impacts since studying particulate matter inhalation is more straightforward than human health impacts from chemicals
Scale of impacts:
Local
Global
Regional
Images source: http://elements.geoscienceworld.org/content/6/4/215/F5.large.jpg

## Slide 6: Size classifications
Particulates classified based on diameter
  Since not perfect spheres, actually based on “hydraulic diameter”
  μm is micrometer (or micron) and equals 10-6 m
Coarse PM: 10 μm to 40 μm
  Too large to significantly penetrate respiratory system
PM10: 2.5 μm to 10 μm
  May get into upper respiratory system
PM2.5: 0.1 μm to 2.5 μm
  May get deep into lungs
Ultrafine PM: <0.1 μm
  May penetrate cell walls
Image source: epa.gov
Increasing Human Health Effect

## Slide 7: Formation of Particulate Matter (PM)
Materials handling
  Crushing
  Loading bulk materials
  Grinding
Wind-blown dust and dirt
Combustion
  Ash (incombustible material)
  Soot (incompletely combusted material)
Formation from gases
  SO2
  NO2
  NH4
  VOCs
Primary particulate matter
Directly released as PM
Secondary particulate matter
PM formed from non-PM precursors
Top: oregrinder.com Middle: senmwx.com

## Slide 8: Secondary Formation
Secondary formation from gases is a major contributor to PM2.5
Depends on atmospheric conditions
Seasonal variation in ability to form secondary PM through various pathways
  NOx and SOx require oxidants and water vapor, so more active in the summer
  NH3 can form ammonium nitrate and ammonium sulfate mostly in the winter
Therefore, emission source profiles and climate/temperature influence secondary PM formation
Sample pathway for NOx:
NOx
Nitric Acid
Reactions with other chemicals
Secondary PM
Mostly mobile sources
Mostly agricultural sources

## Slide 9: Sources
Figure source: EPA. “Understanding Particle Pollution.” www.epa.gov/airtrends/aqtrnd04/pmreport03/pmunderstand_2405.pdf
Natural Sources
(not counted in LCA)
Volcanoes
Forest fires
Windstorms
Pollen
Ocean spray
egu.eu

## Slide 10: Composition of Particulate Matter By US Region
Figure source: EPA. “Understanding Particle Pollution.” www.epa.gov/airtrends/aqtrnd04/pmreport03/pmunderstand_2405.pdf

## Slide 11: Transport
Larger particles settle out relatively quickly
  Minutes to days in the atmosphere
  <100 km travel range
Smaller particles can stay airborne longer and travel a long way in the wind
  Days to weeks in the atmosphere
  About 100-10,000 km range
This is one reason why there are multiple scales of impacts
~10,000 km
~100 km

## Slide 12: Local and Regional Source Contributions
The US EPA compared contributions from local and regional sources
Substantial portions of average concentrations from each source scale
More regional sources in the Eastern US
  Power plants
  Consistently high population density
High proportion local source in Western
Figure source: EPA. “Understanding Particle Pollution.” www.epa.gov/airtrends/aqtrnd04/pmreport03/pmunderstand_2405.pdf

## Slide 13: Human Health Effects
Both short term and long term effects
Short-term
  Decreased lung function
  increased respiratory symptoms
  Cardiac arrhythmias
  Heart attacks
  Premature death
Long-term
  Decreased lung function
  Chronic bronchitis
  Lung cancer
  Premature death
Some populations more susceptible than others
  People with heart/lung disease, elderly, and children
Image source: bcairquality.ca

## Slide 14: Quantified Mortality Risk from Particulate Matter Exposure (Pope III et al. 2002)
Pope III et al. (2002) studied long-term exposure
  Sample size of 500,000 adults over 30 years old from all 50 US states
  Corrected for age, sex, race, weight, height, smoking history, alcohol use, occupational exposures, diet, education, and marital status
  Assessed mortality from three causes: all-cause, cardiopulmonary, and lung cancer compared with PM exposure
Findings
10 μg/L
10 μg/L
PM2.5
4%
All-cause
6%
8%
Cardiopulmonary
Lung Cancer
Pope III, C. A., Burnett, R. T.,…& Thurston, G. D. (2002). Lung cancer, cardiopulmonary mortality, and long-term exposure to fine particulate air pollution. Jama, 287(9), 1132-1141.

## Slide 15: Other Effects of Particulates
Ecosystem and built environment effects are not included in this category for LCA
  Only impacts on human health
Particle pollution also may affect
  Reduced visibility (such as at national parks)
  Affects vegetation and ecosystems, by settling on soil and water
  Damage to man-made structures
Leaves: omafra.gov.on.ca Visibility: EPA. “Understanding Particle Pollution.” www.epa.gov/airtrends/aqtrnd04/pmreport03/pmunderstand_2405.pdf
Cement kiln dust on apple leaves

## Slide 16: Where are there issues with PM in the world?
PM2.5 map: nasa.gov China pop density: china-food-security.org
(averaged over 2001-2006)
Population Density Map of China

## Slide 17: Where are there issues with PM in the US?
Source: nasa.gov
(averaged over 2001-2006)
Top of scale was 80 in last slide

## Slide 18: Characterization of Particulates Potential
HHCAP= Σi (mi x HHCAPi)
where
HHCAP=Human health criteria air pollutants (designation for particulates in TRACI)
mi = mass (in kg) of inventory flow i,
HHCAPi = kg of PM2.5 that have the equivalent health impact of one kg of inventory flow ‘i‘
1 kg of substance | HHCAPi (kg PM2.5-eq)
PM2.5 | 1
PM10 | 0.228
Sulfur dioxide | 0.061
Nitrogen oxides | 0.007
Carbon monoxide | 3.6×10-4
Ammonia | 0.067
HHCAP Characterization Factors (TRACI 2.1)
PM2.5 about 4-5 times as severe as PM10 based on these factors

## Slide 19: Human Health – Particulates
Heart health effects
PM10
Main substances*
Increased human exposure to particulate matter
Midpoint
Fuel combustion
Major sources
Dust from roads
44%
PM2.5
43%
Possible Endpoints
Wood burning
Aggravated asthma
Decreased lung function
SOx
8%
NOx and Others
5%
Dust from fields
Cancer
*Ryberg et al. 2014

## Slide 20: Thank you for completing Module β7!
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules

## Slide 21: Homework
Which would be expected to have a larger impact on human health based on the characterization factors in TRACI 2.1: (a) 1 kg release of PM2.5 or (b) 10 kg release of PM10?
While it would probably not be captured in LCA, how might those releases from question 1 have different impacts on a population of interest located 200 km away from the point of release?
Look at the regional composition of particulate matter in Slide 10 and the sources of those types in Slide 9. Hypothesize why the composition is as shown in the region you live in, if you live in the United States, or choose a region if you live elsewhere.