## Slide 1: Welcome to the Life Cycle Assessment (LCA) Learning Module Series
Acknowledgements:
CESTiCC Washington State University Fulbright
Liv Haselbach Quinn Langfitt
For current modules email haselbach@wsu.edu or visit cem.uaf.edu/CESTiCC

## Slide 2: LCA Module Series Groups
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules

## Slide 3: GREET Tutorial
Module τ3

## Slide 4: Introduction to GREET
Greenhouse gas, Regulated Emissions, and Energy use in Transportation
Developed by Argonne National Lab in 1996, supported by DOE
Over 100 fuel production pathways and 50 vehicle types
Life cycle model in that it takes into account the full system life cycle
Not an LCA tool by ISO 14040 because it does not characterize environmental impacts (no LCIA)
  Useful as a standalone tool
  Frequently used as a data source for transportation LCAs
Available at: https://greet.es.anl.gov/
This module is only an overview. For advanced features refer to the “User Manual” under the “About” menu in the program.

## Slide 5: What will GREET Tell You? (Emissions)
Greenhouse gas emissions
  Carbon dioxide
  Biogenic carbon dioxide
  Methane
  Nitrous oxide
Regulated emissions (basically the criteria air pollutants as defined by EPA)
  Volatile organic compounds (excluding carbon monoxide)
  Carbon monoxide
  Nitrogen oxides
  Sulfur oxides
  Particulate matter (PM2.5 and PM10 separately)
  Gaseous hydrogen

## Slide 6: What will GREET Tell You? (Resource Use)
  Natural gas (renewable, non-renewable)
  Coal (average)
  Crude oil
  Nuclear energy
  Hydroelectric power
  Bituminous oil
  Wind power
  Forest residue
  Geothermal power
  Solar power
  Animal waste
  Uranium ore
  Switchgrass
  Farmed trees
  Fertilizer

## Slide 7: GREET Selection Pane
Well-to-pump
  Impacts to produce fuels and other materials
Well-to-wheel
  Impacts from production and use of fuels
Data editors
  Vehicle mileage, emissions factors for different vehicles, electricity grid mixes, etc.
Simulation parameters
  Modelling year, process input and output editing, crop yields for biofuels feedstocks, heating value, etc.

## Slide 8: Well-to-Pump Pane
Well-to-pump: Impacts from extraction of fuel (i.e. well) to input to vehicle (i.e. pump)
And so on…

## Slide 9: Well-to-pump example: Compressed Natural Gas

## Slide 10: Expanding Processes to See Details

## Slide 11: Well-to-pump example: Functional Unit Choice

## Slide 12: Well-to-pump example: Results

## Slide 13: Well-to-Wheel Pane
Well-to-wheel: Impacts from extraction of fuel (i.e. well) to power to wheels (i.e. wheel)

## Slide 14: Well-to-Wheel Example: Gasoline Car

## Slide 15: Well-to-Wheel Example: Gasoline Car

## Slide 16: Well-to-Wheel Example: Electric Car

## Slide 17: Thank you for completing Module τ3!
Group A: ISO Compliant LCA Overview Modules
Group α: ISO Compliant LCA Detailed Modules
Group B: Environmental Impact Categories Overview Modules
Group β: Environmental Impact Categories Detailed Modules
Group G: General LCA Tools Overview Modules
Group γ: General LCA Tools Detailed Modules
Group T: Transportation-Related LCA Overview Modules
Group τ: Transportation-Related LCA Detailed Modules